Potential Resource Issue:

Aquatic habitat quantity and quality.

Basin Plan objectives compliance.

Project Nexus:

Project operations and potential Project betterments modify or could modify the flow regime in the bypass reaches and the peaking reach, and storage levels in Project reservoirs, thereby influencing instream water temperatures.

Potential License Condition:

- Instream flow releases.

Study Objective(s):

Characterize the relationship between flow and water temperature in bypass reaches and the peaking reach using an appropriate model supported by existing water temperature data.

Characterize water temperature conditions in the bypass reaches and the peaking reach for the existing and unimpaired flow regimes.

Document the availability of cold water temperature refugia in bypass reaches where water temperatures exceed established technical evaluation criteria.

Assess the potential effects of increased air temperature due to global warming on water temperatures over the term of the new Federal Energy Regulatory Commission (FERC) license.

Extent of Study Area:

The study area for water temperature modeling includes: five stream reaches in the Middle Fork American River between French Meadows Reservoir and the confluence with the North Fork American River; two stream reaches in the Rubicon River between Hell Hole Reservoir and Ralston Afterbay; and one reach in the North Fork American River between the Middle Fork American River confluence and Folsom Reservoir (Table AQ4-1 and Figure AQ4-1).  Water temperature models also are proposed for French Meadows and Hell Hole reservoirs.  Duncan Creek and Long Canyon Creek (including the North and South Forks of Long Canyon Creek) will not be included in the temperature modeling study area because Placer County Water Agency (PCWA) has committed to not divert flow from these streams during the summer, after July 1st, in the new license.  The highest summer water temperatures occur in late July and early August (PCWA 2006; PCWA 2007a) and water temperature during this period will not be affected by the Project.  Water temperature monitoring data will continue to be collected for these streams (see PCWA 2007a).

Study Approach:

Summarize water temperature data from the 2005-2006 Water Temperature Study (e.g., PCWA 2006), including seasonal patterns and daily averages, minimums, and maximums as a function of time and location in the bypass and peaking reaches.  Summarize the thermal profiles in the Project reservoirs.  Also summarize the temperature data upstream of Project facilities.  Summarize meteorological conditions (relative humidity, wind speed, solar radiation, air temperature) in the study area based on the meteorological data collected in the 2005-2006 Water Temperature Study (e.g., PCWA 2006).

Continue to collect water temperature and meteorological data through the summers of 2007 and 2008 as part of the Water Temperature Study (PCWA 2007a).  Figure AQ4-2 shows the water temperature and meteorological data collection locations.

Establish a Water Temperature Modeling Subgroup (WTMG) to provide oversight and technical review of modeling procedures/decisions.

Select and develop appropriate reservoir and river water temperature models with seasonal, daily, and within-day temperature modeling capability, as necessary for specific study reaches.  RMA-2 and RMA-11 (King 1994; King 1997) are proposed for the river temperature modeling.  RMA has dynamic flow routing capability and within-day temperature modeling capability.  A new version of HEC-RAS (Brunner 2006) has been released with both dynamic flow routing and temperature modeling capability.  This model may provide a more user friendly temperature and flow modeling platform than the RMA models.  HEC-RAS will be investigated in collaboration with the Aquatic TWG as an alternative to the RMA models.  CE-QUAL-W2 (Cole and Wells 2004) or CE-QUAL-R1 (Environmental Laboratory 1986) will be used for the reservoir water temperature modeling.  CE-QUAL-W2 will be used if suitable bathymetric data are available.  The reservoir temperature models at French Meadows and Hell Hole reservoirs will be integrated to characterize the potential effects on reservoir release temperatures associated with the French Meadows-Hell Hole Pump Storage potential Project betterment.

The models will be developed to simulate average, maximum, and minimum daily water temperature during the summer months when water temperature may be of most concern to aquatic species.  Modeling development steps to be completed in collaboration with the WTMG include:

  - Collect/develop model inputs including channel and reservoir geometry data, solar shading data (topographic and riparian), meteorological data (air temperature, wind speed, relative humidity, solar radiation), hydrology data, and boundary condition flow and water temperature data for the modeled river reaches and reservoirs.

    - Develop channel slopes and reservoir geometry using United States Geological Survey (USGS) Digital Elevation Model (DEM) data.

    - Generate daily and seasonal topographic solar shading data using Geographic Information System (GIS) algorithms and USGS DEM data.  Estimate riparian solar shading using the 2005-2006 Riparian and Aquatic Characterization Study results (PCWA 2007b).

    - Use the 2005-2008 measured Project meteorological data and, if possible, extend the measured meteorological data to the 1975–2004 period through correlation with a long-term meteorological station.  Suitable meteorological stations will be identified and the correlation results will be evaluated as part of this study.

    - Hydrology data will be generated from the operating flow gages during the 2005-2008 period, the Project Operations Model, and from the 1975-2004 existing and unimpaired hydrology developed in the Hydrology Study (2007).

    - Channel cross-section data will be collected in the AQ1 Instream Flow Technical Study Plan (TSP) and extended to the study reaches, as appropriate, using mesohabitat mapping data collected as part of the 2006 Aquatic Characterization Study (PCWA 2007b).

  - Calibrate and validate the hydrodynamics and heat budget portions of the water temperature model(s) with empirical water temperature (river reaches and reservoirs) and meterological data (e.g., use data collected in 2005–2008).  Calibrate water travel time in the peaking reach using the flow fluctuation travel times collected in the AQ1 Instream Flow TSP.

Characterize modeled water temperatures (i.e., seasonal, daily, within-day temperatures) for existing, unimpaired, and alternative flow conditions.  For alternative flow conditions, model a range of flow releases determined by the WTMG.

Incorporate available literature predictions of changes in air temperature as a result of global warming into a limited number of model runs (2-3) to evaluate the resulting effect on water temperature over the anticipated term of the FERC license period (limited sensitivity analysis).

Model the potential effects of the French Meadows-Hell Hole Pump Storage potential Project betterment on reservoir temperature regimes and associated instream release temperatures.

In selected reaches of the lower Rubicon River and the Middle Fork American River, collect water temperature data at tributary inflows and in deep pools to identify the potential availability of water temperature refugia for trout.  In particular, review the 2005-2006 Water Temperature Study results (e.g., PCWA 2006) to identify river reaches with summer temperatures above 20(C.  Within these reaches, identify likely tributaries with potential cold water inflows and characterize the extent of the cold water refugia (e.g., amount of tributary habitat, extent of influence in the main channel).  Identify two deep pools upstream and two downstream of the tributary and collect water temperature profiles to examine potential thermal stratification.

In the Project reaches where water temperature will not be modeled (e.g., Duncan Creek, North Fork Long Canyon Creek, South Fork Long Canyon Creek, and Long Canyon Creek), use existing water temperature and meteorological data to quantify the relationships between air temperature and water temperature.

Schedule:

| Date | Activity |
| --- | --- |
| January through October 2008 | Develop and validate preliminary temperature model in collaboration with the Aquatic TWG |
| November 2008 through June 2009 | Analyze data, develop the water temperature analysis in collaboration with the Aquatic TWG, and prepare draft report |
| July 2009 | Distribute draft report to the Aquatic TWG |
| July through September 2009 | Aquatic TWG 90 day review and comment period |
| October through December 2009 | Resolve comments and prepare final report |
| January 2010 | Distribute final report to the Aquatic TWG and Plenary |

Level of Effort and Cost:

To be determined.

References:

Brunner, G. W.  2006.  HEC-RAS River Analysis System User’s Manual (Version 4.0 Beta).  US Army Corps of Engineers Hydrologic Engineering Center (HEC).

Cole, T. M. and S. A. Wells.  2004.  CE-QUAL-W2: A Two-Dimensional, Laterally Averaged, Hydrodynamic and Water Quality Model, Version 3.2.  User Manual; Instruction Report EL-03-1. U.S. Army Corps of Engineers, Washington, DC.

Environmental Laboratory.  1986.  CE-QUAL-R1: A numerical, one-dimensional model of reservoir water quality; User’s Manual, Instructional report EL-82-1 (Revised Edition), U.S. Army Corps of Engineer Waterways Experiment Station, Vicksburg, MS.

King, I.P.  1994.  RMA-2: A Two-Dimensional Finite Element Model for Flow in Estuaries and Streams, Version 5.1.  Department of Civil and Environmental Engineering, University of California, Davis.

King, I.P.  1997.  RMA-11: A Three Dimensional Finite Element Model for Water Quality in Estuaries and Streams – Documentation Version 2.5.  Department of Civil and Environmental Engineering, University of California, Davis.

Placer County Water Agency (PCWA).  2006.  Middle Fork American River Hydroelectric Project (FERC No. 2079), Final 2005 Water Temperature Study Report.

Placer County Water Agency (PCWA).  2007a.  Middle Fork American River Hydroelectric Project (FERC No. 2079), Final 2006 Water Temperature Study Report.  April, 2007.

PCWA.  2007b.  Placer County Water Agency Middle Fork American River Project (FERC No. 2079) 2006 Physical Habitat Characterization Study Report.  April, 2007.

Table AQ4-1.	Water Temperature Modeling Reaches.

| Study Reach | Bypass Reaches | Peaking Reach | Reservoir | Water Temperature Modeling |
| --- | --- | --- | --- | --- |
| Duncan Creek |  |  |  |  |
| Duncan Creek from Diversion to confluence with Middle Fork American River | ( |  |  | No |
| Middle Fork American River |  |  |  |  |
| French Meadows Reservoir |  |  | ( | Yes |
| Middle Fork American River from French Meadows to confluence with Duncan Creek | ( |  |  | Yes |
| Middle Fork American River from confluence with Duncan Creek to Middle Fork Interbay | ( |  |  | Yes |
| Middle Fork Interbay |  |  | ( | Yes1 |
| Middle Fork American River from Middle Fork Interbay to Ralston Afterbay | ( |  |  | Yes |
| Ralston Afterbay Downstream |  |  |  |  |
| Ralston Afterbay |  |  | ( | Yes1 |
| Middle Fork American River from Ralston Afterbay to confluence with Canyon Creek |  | ( |  | Yes |
| Middle Fork American River from confluence of Canyon Creek to confluence with North Fork American River |  | ( |  | Yes |
| North Fork American River from confluence with Middle Fork American River to Folsom Reservoir |  | ( |  | Yes |
| Rubicon River |  |  |  |  |
| Hell Hole Reservoir |  |  | ( | Yes |
| Rubicon River from Hell Hole Reservoir to confluence with South Fork Rubicon River | ( |  |  | Yes |
| Rubicon River from confluence with South Fork Rubicon River to Ralston Afterbay | ( |  |  | Yes |
| Long Canyon Creek |  |  |  |  |
| North Fork Long Canyon Creek from Diversion to confluence with Long Canyon Creek | ( |  |  | No |
| South Fork Long Canyon Creek from Diversion to confluence with Long Canyon Creek | ( |  |  | No |
| Long Canyon Creek from North and South Fork Long Canyon creeks confluence to confluence with Rubicon River | ( |  |  | No |

1These small reservoirs will be modeled using the river temperature model.

Placeholder for Figure AQ4-1 Temperature Modeling Study Reaches Non-Internet Public Information

This Figure has been removed in accordance with the Commission regulations at 18 CFR Section 388.112. This Figure is considered Non-Internet Public information and should not be posted on the Internet. This information may be accessed from the Placer County Water Agency’s (PCWA’s) Public Reference Room, but is not expected to be posted on PCWA’s Website, except as an indexed item.