Potential Resource Issue:

Macroinvertebrate community distribution and abundance and special-status aquatic mollusk presence or absence.

Project Nexus:

Project operations and Project betterments modify or could potentially modify flow regimes and water quality (including water temperature) in the bypass reaches and the peaking reach, potentially affecting the macroinvertebrate community and food availability for fish.

If special-status aquatic mollusk species are present, Project operations and Project betterments could potentially modify their habitat or affect their populations.

Potential License Condition:

Instream flow releases.

Site-specific water quality measures.

Study Objective(s):

Document the seasonal density and size distribution of drifting macroinvertebrates in selected bypass reaches and the peaking reach for input to bioenergetics growth and habitat modeling.

Document the benthic macroinvertebrate community in the peaking reach and compare to adjacent bypass and comparison reaches to characterize general habitat conditions.

Sample the benthic macroinvertebrate community at long-term USDA Forest Service sampling sites to supplement existing data sets.

Document the benthic macroinvertebrate community in the bypass reaches downstream of each large reservoir (Middle Fork American River below French Meadows Reservoir and Rubicon River below Hell Hole Reservoir).

Document the benthic macroinvertebrate community in areas with known water quality issues as determined in the AQ 11 – Water Quality Technical Study Plan (TSP).

Determine the presence or absence of three special-status mollusk species (California Floater, Anodonta californiensis, scalloped juga, Juga occata, and Great Basin ramshorn’s snail, Helisoma newberry newberry) and identify potentially suitable habitat for these species (Furnish 2005).

Extent of Study Area:

The study area includes accessible bypass reaches, the peaking reach, and potential comparison reaches identified in Table AQ 3-1 and Figure AQ 3-1.

Study Approach:

Macroinvertebrate Drift Sampling for input to Bioenergetics Modeling

Collect drift samples at select AQ 1 – Instream Flow TSP sites (Table AQ 3-1 and Figure AQ 3-1).  Identify two representative riffles and sample drift at the downstream end of each riffle.  Collect three drift samples at each riffle using a sampling methodology similar to that used in Hayes et al. 2000.  Daytime only drift samples will be collected.

Collect drift samples at three different times (June, August, and October).  Process samples based on average drift density (number/m3) at each site by 2 mm prey size classes (e.g., lengths 1-3 mm, 3-5 mm, 5-7 mm, etc.).  Use general aquatic invertebrate length versus weight relationships to convert macroinvertebrate drift to energy equivalents (joules/m3/size class) for bioenergetics modeling.

Compare/contrast drift density and size between the study reaches and with the literature.

Use the drift density information as an input to bioenergetics models to assist in the identification of limiting factors related to fish growth (food, water temperature, habitat) (see AQ 5 – Bioenergetics TSP).

Benthic Macroinvertebrate Sampling for General Habitat Conditions

In the bypass, peaking, and comparison reaches collect benthic samples and inventory data following the California Stream Bioassessment Procedure (CSBP) (CDFG 2003).  Collect composite riffle samples in October, process samples, and perform taxonomic identification according to CSBP protocols (CDFG 2003).  Report benthic macroinvertebrate metrics as outlined in Rehn et al. (in review) as part of the data summary and provide other benthic maroinvertebrate metrics requested by the Aquatic TWG. Statistically compare/contrast CSBP sampling results between reaches and with values reported in the literature.  Proposed sampling sites for benthic macroinvertebrates are identified in Table AQ 3-1 and Figure AQ 3-1.

Peaking Reach

Conduct CSBP sampling in the peaking reach and adjacent bypass and comparison reaches (the Middle Fork American and Rubicon rivers above Ralston Afterbay, the North Fork of the Middle Fork American River, and the North Fork American River) to compare and contrast the macroinvertebrate communities.

    - To ensure comparability, select sample locations in the peaking reach and in the comparison reaches that are similar in substrate and hydraulic characteristics.

    - Include and augment the ongoing Ralston Sediment Management Project fall CSBP sampling and sampling locations (Jones & Stokes 2002; Jones & Stokes 2006) within this sampling protocol (Table AQ 3-1).  The existing Jones & Stokes (2006) CSBP sampling sites will be sampled.  The new sampling locations to augment the existing data will be located within the AQ 1 – Instream Flow TSP study sites where possible.  Jones & Stokes staff will be integrated into the data collection at these sites to ensure data consistency between sites and with historical samples.

Long-Term Agency and below Large Reservoir Sampling Sites

Conduct CSBP sampling at the long-term agency sampling sites above and below the diversions on Duncan and South Fork Long Canyon creeks.

Conduct CSBP sampling downstream of French Meadows Reservoir on the Middle Fork American River and downstream of Hell Hole Reservoir on the Rubicon River.

Special-status Aquatic Mollusks Sampling

- Identify potential habitat using aerial photographs, helicopter video, Project maps, USGS 7.5 minute topographic maps, existing literature, and archeological information (e.g., mussel shells).

- Determine the number and location of representative survey sites based on the extent of identified suitable habitat.  Presently, 20 survey sites have been identified (Figure AQ 3-2).  The mollusk sampling sites are co-located at the benthic macroinvertebrate sampling sites (Table AQ 3-1) and AQ 1 – Instream Flow TSP study sites. Sites are also located at the main tributary inflow locations of French Meadows and Hell Hole reservoirs.  Also, if mussel shells are observed at fish sampling sites (see AQ 2 – Fish Population TSP) and/or at foothill yellow-legged frog survey sites (see AQ 12 – Special-Status Amphibian and Aquatic Reptile TSP), mollusk sampling sites will be added at these locations.  If the potential habitat evaluation identifies other mollusk survey sites (e.g., perennial springs or archeological sites with shells), then these sites will be surveyed.

- Survey sites will be a minimum of 100 m in length and surveyed in an upstream direction on each side of the river. River edges will be surveyed to a depth of approximately 60 cm. A viewing tube or snorkeling will be used to survey the deeper water. All substrates will be sampled.  Sub-sampling will be used if necessary.  If mud or silt substrate is present, then it will be sub-sampled at several locations using sieving.

- All site surveys will be timed and surveyed for a minimum of two hours.

- Physical habitat characteristics will be collected (water temperature, substrate composition, water velocity, and estimated channel gradient, width, and mean depth) at each study site.

- Aquatic gastropods will be field identified to family, genus, or species using keys in Burch (1989), McMahon (1991), and Frest and Johannes (1999) and representative specimens will be collected and preserved for laboratory verification.

- Mussels will be field identified using keys in Burch (1975 a, b) and McMahon (1991), and shells will be collected if present for further identification.

Data

All data (drift, benthic invertebrate, and mollusk) will be provided to the Aquatic TWG in an Excel spreadsheet electronic format.

Contingency Sampling

Coordinate with the AQ 11 – Water Quality TSP to identify any additional CSBP sampling locations based on water quality results.

Schedule:

| Date | Activity |
| --- | --- |
| June 2007 | In consultation with the Aquatic TWG select macroinvertebrate sampling sites |
| June 2007 | Conduct drift sampling |
| August 2007 | Conduct drift sampling |
| September and October 2007 | Conduct benthic and drift sampling |
| November 2007 through March 2008 | Analyze data and prepare draft report |
| April 2008 | Distribute draft benthic and drift sampling report to the Aquatic TWG |
| April and May 2008 | Aquatic TWG 60 day review and comment period |
| June and July 2008 | Resolve comments and prepare final report |
| August 2008 | Distribute final benthic and drift sampling report to the Aquatic TWG and Plenary |
| August 2008 | Where appropriate conduct mollusk sampling |
| September 2008 through June 2009 | Conduct contingency macroinvertebrate sampling, data analysis and report production |
| February 2009 | Distribute draft mollusk sampling report to the Aquatic TWG |
| February and March 2009 | Aquatic TWG 60 day review and comment period |
| April and May 2009 | Resolve comments and prepare final report |
| June 2009 | Distribute final mollusk report to the Aquatic TWG and Plenary |

Level of Effort and Cost:

To be determined.

References:

California Department of Fish and Game (CDFG).  2003.  California stream bioassessment procedure (Protocol brief for biological and physical/habitat assessment in wadeable streams).

Burch, J. B. 1975a. Freshwater sphaeriacean clams (Mollusca: Pelecypoda) of North America. Prepared in 1972 for the U.S. Environmental Protection Agency as Identification Manual No. 3 Biota of Freshwater Ecosystems, Malacological Publications, Hamburg, Michigan. 96 pp.

Burch, J. B. 1975b. Freshwater unionacean clams (Mollusca: Pelecypoda) of North America. Prepared in 1973 for the U.S. Environmental Protection Agency as Identification Manual No. 11 Biota of Freshwater Ecosystems, Malacological Publications, Hamburg, Michigan. 204 pp.

Burch, J.B. 1989. North American freshwater snails. Malacological Publications, Hamburg, Michigan. viii + 365pp.

Frest, T. J., and E. J. Johannes. 1999. Field guide to survey and manage freshwater mollusk species. September 30, 1999. Bureau of Land Management, U. S. Fish and Wildlife Service, U. S. Forest Service, BLM/OR/WA/PL-99/045+1792.117 pp.

Furnish, J.  2005. Guide to sensitive aquatic mollusks of the U.S. Forest Service Pacific Southwest Region.  USDA Forest Service, Pacific Southwest Region.

Hayes, J.W., J.D. Stark, K.A. Shearer.  2000.  Development and test of a whole-lifetime foraging and bioenergetics growth model for drift-feeding brown trout.  Trans. Am. Fish. Soc. 129:315-332.

Jones & Stokes.  2002.  Ralston Afterbay sediment management project Indian Bar Pilot Project. Jones & Stokes, Sacramento, CA.

Jones & Stokes.  2006. Draft water quality and aquatic resources monitoring program for the Ralston Afterbay sediment managemnt project—2005 Annual Report. August. (J&S 05596.05.) Sacramento, CA.

McMahon, R. F. 1991. Mollusca: Bivalvia. Pages 315-399 in J. H. Thorp and A. P. Covich, editors. Ecology and classification of North American freshwater invertebrates. Academic Press, San Diego, California. 911 pp.

Rehn, A. C., N. Ellenrieder, and P. R. Ode.  In review.  Assessment of Ecological Impacts of Hydropower Projects on Benthic Macroinvertebrate Assemblages:  A Review of Existing Data Collected for FERC Relicensing Studies.  California Energy Commission, contract #500-03-017.

Table AQ 3-1.	Macroinvertebrate Sampling Reaches.

| Study Reach | Bypass Reaches | Peaking Reach | Comparison Reach | Long-Term Agency Sampling Sites | Number of Benthic Macroinvertebrate Sample Locations (River Mile) | Number of Drift Macroinvertebrate Sample Locations (River Mile) | Jones & Stokes (2002, 2006) Ongoing Benthic Macroinvertebrate Sample Locations (Transects) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Duncan Creek |  |  |  |  |  |  |  |
| Duncan Creek upstream of Diversion |  |  |  | ( | 1 (D9.0) | -- | -- |
| Duncan Creek from Diversion to confluence with Middle Fork American River | ( |  |  | ( | 1 (D8.3 or D6.3) | -- | -- |
| Middle Fork American River |  |  |  |  |  |  |  |
| Middle Fork American River from French Meadows Reservoir to Interbay | ( |  |  |  | 1 (MF44.7) | -- | -- |
| Middle Fork American River from Middle Fork Interbay to Ralston Afterbay | ( |  |  |  | 1 a (MF26.2) | 1 (MF26.2) | 1 (Transects 25, 27, 29) |
| Middle Fork American River from Ralston Afterbay to confluence with Canyon Creek |  | ( |  |  | 1 a (MF14.1 and MF21.0) | 1 (MF14.1 and MF21.0) | 3 b (Transects 1, 3, 7, 9, 11, 13, 16, 18, 20, 23) |
| Middle Fork American River from confluence of Canyon Creek to confluence with North Fork American River |  | ( |  |  | 1 (MF4.8) | 1 (MF4.8) | -- |
| Rubicon River |  |  |  |  |  |  |  |
| Rubicon River from Hell Hole Reservoir to confluence with South Fork Rubicon River | ( |  |  |  | 1 (R25.7) | 1 (R25.7) | -- |
| Rubicon River from confluence with South Fork Rubicon River to Ralston Afterbay | ( |  |  |  | 2 a (R20.9 and R1.2) | 2 (R20.9 and R1.2) | 1 (Transects 36, 40, 43) |
| Long Canyon Creek |  |  |  |  |  |  |  |
| South Fork Long Canyon Creek upstream of Diversion |  |  |  | ( | 1c (SFLC4.2) | -- | -- |
| South Fork Long Canyon Creek from Diversion to confluence with Long Canyon Creek | ( |  |  | ( | 1c (SFLC2.3) | -- | -- |
| Other Tributaries |  |  |  |  |  |  |  |
| North Fork of the Middle Fork American River |  |  | ( |  | 1 a (NFMF2.4) | -- | 1 (Transects 31, 33, 35) |
| North Fork American River |  |  | ( |  | 1 (NF31.3) | -- | -- |

aSome of these samples would be in approximately the same area as the Jones & Stokes ongoing monitoring, but would enhance that sampling effort. bOne sampling location is split into two locations above and below the confluence of North Fork Middle Fork American River
  confluence.

cSamples on the South Fork Long Canyon Creek above and below the diversion will be used as surrogates for the North Fork Long Canyon Creek above and below the diversion.  The Star Fire in 2001 may have affected the benthic macroinvertebrate community in North Fork Long Canyon Creek.

Placeholder for Figure AQ 3-1 Macroinvertebrate Study Reaches Non-Internet Public Information

This Figure has been removed in accordance with the Commission regulations at 18 CFR Section 388.112. This Figure is considered Non-Internet Public information and should not be posted on the Internet. This information may be accessed from the Placer County Water Agency’s (PCWA’s) Public Reference Room, but is not expected to be posted on PCWA’s Website, except as an indexed item.

# Footnotes

Special-status species is defined as any species that is listed as rare, threatened, or endangered or as a species of special concern by a federal, state, or local agency. The species identified are US Forest Service sensitive species.