APPENDIX A

Pictorial of the Hydroacoustics Sampling Design

The following is a brief pictorial of the hydroacoustics sampling design that will be used to detect the number of fish entering the intakes at Ralston Afterbay and Middle Fork Interbay.  Three split-beam transducers will be ‘fixed’ or attached to the inside of the trash racks of the tunnel intakes at both Ralston Afterbay and Middle Fork Interbay dams.  Schematics illustrating the hydroacoustic sampling design are shown in Figures 1 though 4.

To determine the risk of entrainment, the direction that a fish is traveling and its depth location relative to the intakes is assessed.  The direction of fish travel within the acoustic beam is translated into a compass angle.  Fish that are traveling at angles towards the intake (see example histogram in Figure 5) and are at the depth of the intake are assumed to be entrained (Figure 6).

Figure 1.	Picture Illustrating the Hydroacoustic Sampling Design at Ralston - Oxbow Tunnel Inlet Structure.

Figure 2.	General Schematic Illustrating the Orientation of Acoustic Beam and Sample Volume at each intake.

Intake 	Side View		    			     Intake Front View

I

Figure 3.	Picture showing the Middle Fork - Ralston Tunnel Inlet Structure.

Note: Trash racks are below the water’s surface.  Refer to Figure 1 for a similar design at Ralston Afterbay.

Figure 4.	Cross-sectional Top View of the Acoustic Beams Showing the Sectors (Blue Color) Where Fish Have a Risk of Entrainment.

Figure 5.	Example Summary Data of the Number of Fish at Risk of Entrainment Based on the Direction of Fish Travel.

Figure 6.	Assessment of Risk of Entrainment Based on Fish Direction of Travel and Depth.

References

BioSonics. 2008.  What is hydroacoustics.  Available at http://www.biosonicsinc.com/resources/what_is_hydroacoustics.html).  Accessed August 2008.

# Text boxes

Transducers

Inside Trash Rack

Trash Rack

Number of fish at risk of entrainment

Acoustic Beams Inside Intake Structure

Example of a Transducer

Transducers – mounted on trash racks.  Acoustic beams are underwater.

Hypothetical depth of intake

315

0

0

Modified from BioSonics

Modified from BioSonics

Modified from BioSonics

BioSonics

90

135

225

180

270

45

Flow

Trash Rack

Cross-section of Acoustic Beams

Intake

Intake

Transducer

Normal Lower Pool Level

Normal Upper Pool Level

Intake

Flow

Trash Rack

Acoustic Beam