Placer County Water Agency

Middle Fork American River Project

(FERC Project No. 2079)

Operations Simulation Model

Sample Input and Output Handout Packet

Placer County Water Agency

144 Ferguson Road

Auburn, CA  95604

January 16, 2008

Article 37.  The Licensee shall release from Duncan Creek Diversion Dam, French Meadows Dam, Hell Hole Dam, South Long Canyon Diversion Dam, North Long Canyon Diversion Dam, Ralston or Middle Fork Interbay, and Oxbow Powerplant, sufficient flows to meet the following schedule:

| Location | Forecasted Runoff to Folsom Reservoir in Acre-Feet | Streamflow in Cubic Feet Per Second |
| --- | --- | --- |
| Duncan Creek Diversion Dam | 1,000,000 or more | 8, or the natural flow, whichever is less |
|  | Less than 1,000,000 | 4, or the natural flow, whichever is less |
| French Meadows Dam | 1,000,000 or more Less than 1,000,000 | 8, at all times 4, at all times |
| Hell Hole Dam | 1,000,000 or more | 20, May 15 thru December 14 10, December 15 thru May 14 |
|  | Less than 1,000,000 | 10, June 1 thru October 14 6, October 15 thru May 31 |
| South Long Canyon Diversion Dam | 1,000,000 or more | 5, or the natural flow, whichever is less |
|  | Less than 1,000,000 | 2.5, or the natural flow, whichever is less |
| North Long Canyon Diversion Dam | Any forecast | 2, or the natural flow, which is less |
| Ralston or Middle Fork Interbay | 1,000,000 or more | 23, or the natural flow, whichever is less |
|  | Less than 1,000,000 | 12, or the natural flow, whichever is less |
| Oxbow | Any forecast | 75, year round |

MFP Model Variable Inputs

Minimum instream flow requirements:

Input tables will allow requirements to vary by month and by year type (wet, above average, below average, dry and critical dry).

- Duncan Creek Diversion Dam

- French Meadows Dam

- Hell Hole Dam

- South Fork Long Canyon Diversion Dam

- North Fork Long Canyon Diversion Dam

- Middle Fork Interbay Dam

- Ralston Afterbay Dam

Minimum Storage levels at French Meadows and Hell Hole Reservoirs:

Input tables will allow requirements to vary by month and by year type.

Maximum ramping rates below Oxbow Powerhouse: cfs per hour

Consumptive Water Demands:

Annual demands are spread monthly based upon a standard monthly urban demand curve.

- Consumptive diversions at Auburn

- Consumptive diversions at Folsom

Normal End of Year Target Carryover Storage Volume:

Water Forum Dry Year Release and Reclamation Refill Requirements: on/off

Maintenance Period and Length:

MFP Model Standard Steering Committee Output List

List any Violations of Input “Requirements”:

Storage:

At French Meadows and Hell Hole Reservoirs –

- Storage

- Spills

At Middle Fork Interbay and Ralston Afterbay –

- Spills

Oxbow Powerhouse and Ralston Afterbay:

- Oxbow powerhouse flows (with ramping rates),

- Ralston Afterbay Storage

- Ralston Powerhouse flows

- Recreation flows

Diversion Flows:

- Duncan Creek

- South Fork Long Canyon Creek

- North Fork Long Canyon Creek

Generation:

Total monthly generation in MWHr by category of Peak Hours, Partial-Peak Hours, Off-Peak Hours and Super-Off-Peak Hours, and by powerhouse

In addition to the above suggested standard outputs the complete output of flows, both natural and operational at every identified location is available.

Steering Committee Input – Output Worksheets

The following four worksheets are used for input requests.

The following three sheets are summary output.