Table AQ 1-5. Target and Actual Instream Flow Modeling Calibration Flows by Facility. Facility/ Location Current FERC License Instream Flow Requirement1 Target Calibration Flow/Release2 Actual Calibration Flow/Release Duncan Creek Diversion Dam Dry: 4 cfs or natural Wet: 8 cfs or natural 4-8, 163, 44 3-4, 11-173, 51-54 North Fork Long Canyon Diversion Dam All Times: 2 cfs or natural 2, 53, 11 2, 53, 15 South Fork Long Canyon Diversion Dam Dry: 2.5 cfs or natural Wet: 5 cfs or natural 2.5-5, 103, 21 7, 183, 29 Long Canyon Creek None 4.5-7, 153, 47.5 (NF and SF releases above plus natural accretion) 17, 273, 53 French Meadows Dam Dry: 4 cfs Wet: 8 cfs 4-8, 483, 187 10-16, 54-643, 181-225 Middle Fork Interbay Dry: 12 cfs or natural Wet: 23 cfs or natural 12-23, 1003, 3744 17-24, 903, 188 Below Oxbow Powerhouse All Times: 75 cfs bl. NF of MF Confluence 75, 3683, 10003, 101-111, 393-4533, 910-1040 Hell Hole Dam Dry: 10 cfs June 1 – Oct 14 6 cfs Oct 15 – May 31 Wet: 20 cfs May 15 – Dec 14 10 cfs Dec 15 – May 14 10-20, 803,5, 3155 23, 663,5, 775 Rubicon River Below South Fork Rubicon River None 10-206, 1046, 3706 32-49, 77-863, 130-218 1CDWR current year forecast of unimpeded run-off of the American River to Folsom Reservoir: Dry <1,000,000 a/f, Wet > 1,000,000 a/f. 2These are target flows identified by the Aquatic TWG. 3Flows for velocity data collection. 4The canyon is narrow in this reach and 374 cfs may be too high to safely work in the channel. A flow release will be made as close to 374 cfs as can be safely worked. 5The facilities at Hell Hole Dam are limited in their release capabilities. The medium flow was reduced to approximately 65 cfs. The highest possible flow was released. The Aquatic TWG was informed regarding the flows to be released and consulted regarding hydraulic model development options. 6Hell Hole release plus natural accretion. This is an approximate target.