Appendix C

Qualitative Fish Population Sampling: Survey Notes from Sampling Upstream of Small Stream Diversion Structures and Spring Fry Sampling Results

Table of Contents

Page

Survey Notes of the Fish Distribution Sampling in South Fork Long Canyon Creek, North Fork Long Canyon Creek, and Duncan Creeks Upstream of the Diversions	1

South Fork Long Canyon Creek	2

North Fork Long Canyon Creek	7

Little Duncan Creek	12

Duncan Creek	17

List of Tables

Table C-1.	The Upstream Extent of the Fish Distribution in South Fork Long Canyon, North Fork Long Canyon, and Duncan Creeks above the Diversion Dams.

Table C-2.	Summary of the Upstream Distribution Sampling for South Fork Long Canyon, North Fork Long Canyon, and Duncan Creeks above the Diversion Dams.

Table C-3.	Minimum and Maximum Fork Lengths of Fish Species Caught during Qualitative Sampling for Young-of-the-Year.

List of Maps

Map C-1.	2007 Trout Survey Upper Long Canyon Area.

Map C-2.	2007 Trout Survey Duncan Creek Area.

# Survey Notes of the Fish Distribution Sampling in South Fork Long Canyon Creek, North Fork Long Canyon Creek, and Duncan Creeks Upstream of the Diversions

Fish distribution surveys of South Fork Long Canyon Creek, North Fork Long Canyon Creek, Duncan Creek, and Little Duncan Creek were conducted to determine the upstream limit of trout above the diversions.  Surveys dates were between 8/13/2007 and 8/16/2007.  Two surveyors followed the creek channel and sampled representative pools until the uppermost pool containing trout was reached.  The dimensions (length, width, and maximum depth) of all pools, and discharge of the lower elevation pools were measured.  The discharge at the pools farther upstream (higher elevation pools) was too small/shallow to be measured.  Fish surveys were conducted by visual counts as the leading surveyor approached the pool or by snorkel.  The counts were calibrated by conducting visual surveys and single pass electrofishing at three pools.  Fish were identified to species and categorized into two age classes Young-of-the-Year (YOY) and juvenile/adult.

Rainbow trout were observed in both South Fork Long Canyon Creek and North Fork Long Canyon Creek. Rainbow trout and brown trout were observed in Duncan Creek and Little Duncan Creek.  The numbers of trout observed in each pool loosely correlated with the size of the pool and the magnitude of inflow.  A gradual decrease in flow and habitat connectivity was observed as the upstream limit of trout presence was approached.  The upper limit of trout was pinpointed for all four streams sampled.  Trout inhabited a majority of available habitats.  In Duncan Creek and North Fork Long Canyon Creek trout were present until the stream habitat became too shallow or intermittent.  In South Fork Long Canyon Creek and Little Duncan Creek the distribution ended at small barriers.  It appeared, however, that these barriers limited the distribution due to insufficient flows.  The exact upstream limits of trout on all four surveyed creeks may vary between years based on water year type, the magnitude of high spring flows, and the persistence of summer flows.

# South Fork Long Canyon Creek

surveyed 8/13/2007

River Mile 5.75

Habitat Type: Plunge pool

Notes: Culvert forms a barrier at low flows

Dimensions: Drop pool is 5.5’ deep 25-30’ wide, 35’ long

Fish Count: Approximately 40 Rainbow Trout (RBT) yearling to adult age range

Flow: 0.13 cfs

South Fork Long Canyon Creek

surveyed 8/13/2007

River Mile 5.8

Habitat Type: Pool

Notes: None

Dimensions: 15’ wide, 30’ long, 2’ deep

Fish Count: Approximately 15 yearling to adult, 12 young of the year (YOY)

Flow: 0.09 cfs

South Fork Long Canyon Creek

surveyed 8/13/2007

River Mile 8.1

Habitat Type: Pool

Notes: None

Dimensions: 15’ long, 6’ wide, 0.95’ deep

Fish Count: Approximately 5 RBT YOY to yearling age range

Flow: Not measurable, stream is intermittent

River Mile 8.3

Habitat Type: Pool

Notes: None

Dimensions: Not Available

Fish Count: 1 adult RBT present. Approximately 75 YOY were present in ~400 yards of intermittent pools and riffles

Flow: Not measurable

South Fork Long Canyon Creek

surveyed 8/13/2007 (continued)

River Mile 8.55

Upstream limit of trout in South Fork Long Canyon Creek (survey continued 0.85 miles upstream)

Habitat Type: Pool

Notes: None

Dimensions: 1’ deep, 15’ wide, 15’ long. 6’ tall debris jam at head of pool may act as a barrier

Fish Count: 1 yearling RBT

Flow: Not measurable

South Fork Long Canyon Creek

surveyed 8/13/2007

River Mile 9.4

Habitat Type: Intermittent small pools

Notes: None

Dimensions: Not Available

Fish Count: No fish

Flow: No surface flow

# North Fork Long Canyon Creek

surveyed 8/14/2007

River Mile 3.6

Habitat Type: Pool

Notes: Pool was electrofished with a single thorough pass. We compared electrofishing count with visual estimate at three pools

Dimensions: 12’ wide, 22’ long, 1.1’ deep.

Fish Count: 	Visual - 3 yearling to adult, 2 YOY
E-fishing - 1 adult, 1 yearling, 2 YOY

Flow: 0.2 cfs

North Fork Long Canyon Creek

surveyed 8/14/2007

River Mile 3.6

Habitat Type: Pool

Notes: None

Dimensions: 13’ wide, 20’ long, 1.7’ deep

Fish Count: 	Visual - 3 YOY, 10 yearling to adult
E-fishing 3 YOY, 8 yearling, 1 adult

Flow: Same as pool 1.

North Fork Long Canyon Creek

surveyed 8/14/2007

River Mile 3.6

Habitat Type: Pool

Notes: None

Dimensions: 12’ wide, 25’ long, 2.6’ deep

Fish Count:	Visual - 6-8 YOY, 3 yearling, 2 adult
E-fishing - 6 YOY, 3 yearling, 1 adult, 5-6 yearling to adult were missed

Flow: Same as pool 1

Note: A trial comparison shows that an initial visual count of trout present in the pool had roughly the same accuracy as single pass electrofishing. Visual counts of trout in pools had to be done quickly by the first person to encounter the pool as trout would scatter and hide very quickly.  Visual counts from the surface were not able to determine species. In some pools a mask and snorkel were used and species could be identified.

North Fork Long Canyon Creek

surveyed 8/14/2007

River Mile 4.3

Habitat Type: Pool

Notes: Mid-channel pool

Dimensions: 19’ wide, 34’ long, 4.5’ deep

Fish Count: 2 YOY, 14 yearling to adult

Flow: 0.09 cfs

River Mile 4.8

Habitat Type:

Notes: None

Dimensions: 7’ wide, 12’ long, 0.85’ deep

Fish Count: 3 YOY

Flow: Not measurable

North Fork Long Canyon Creek

surveyed 8/14/2007

River Mile 4.9

Upstream limit of trout in North Fork Long Canyon Creek
(survey continued 0.2 miles upstream)

Habitat Type: Isolated pool

Notes: Heavy algal growth, temperature very stratified, channel mostly dry upstream

Dimensions: 6’ wide, 16’ long, 1’ deep

Fish Count: 3 YOY, 1 yearling

Flow: No surface flow

# Little Duncan Creek

surveyed 8/15/2007 and 8/16/2007

River Mile 0.45

Habitat Type: Pool

Notes: Creek is very high gradient through this reach with steep bedrock cascades and scour pools and numerous potential migration barriers

Dimensions: Pool 25’ wide, 45’long, 4’ deep

Fish Count: 6 YOY

Flow: 0.07 cfs

Little Duncan Creek

surveyed 8/15/2007 and 8/16/2007

River Mile 0.8

Habitat Type: Pool

Notes: None

Dimensions: 18’ wide, 35’long, 2.25’ deep

Fish Count: 2 adult

Flow: Not measurable

Little Duncan Creek

surveyed 8/15/2007 and 8/16/2007

River Mile 1.2

Habitat Type: Pool

Notes: Confluence of Little Duncan Creek (LDC) headwater and Little Robinson Valley (LRV) headwater. No fish detected on LRV creek ~200 meters above the confluence. Bedrock sheet cascade on LRV creek may be migration impediment

Dimensions: 8’ wide, 20’ long, 1.0’ deep

Fish Count: 2 YOY

Flow: Not measurable

Little Duncan Creek

surveyed 8/15/2007 and 8/16/2007

River Mile 1.2 – Pool 4

Habitat Type: Pool

Notes: LDC headwater above confluence with LRV creek

Dimensions: 7.5’ wide, 17’ long, 0.9’ deep

Fish Count: 2 YOY

Flow: Not measurable

Little Duncan Creek

surveyed 8/15/2007 and 8/16/2007

River Mile 1.3 – Pool 5

Upstream limit of trout in Little Duncan Creek (survey continued 1.4 miles upstream)

Habitat Type: Bedrock Pool

Notes: Upstream passage blocked by steep bedrock sheet cascade. Downstream passage blocked at low flow by cobbles, boulders, and debris. Flow is not measurable.  Very low surface flow extends upstream from this pool. Higher bedrock barriers below this point did not appear to affect the distribution of trout. Perhaps there was insufficient flow depth for adult fish to pass this barrier.

Dimensions: 25’ wide, 20’ long, 4.2’ deep

Fish Count: 1 yearling unidentified trout, 1 large adult Brown Trout (BNT)

Flow: Not Available

# Duncan Creek

surveyed 8/16/07

River Mile 12.4

Habitat Type: Step-Pool

Notes: None

Dimensions: 10’ wide, 28’ long, 1.0’ deep

Fish Count: 2 yearling to adult, 1 YOY

Flow: 0.13 cfs

Duncan Creek

surveyed 8/16/07

River Mile 12.5

Habitat Type: Pool

Notes: None

Dimensions: 21’ wide, 60’ long, 1.6’ deep

Fish Count: Approximately 10 yearling to adult

Flow: Similar to pool 1

Duncan Creek

surveyed 8/16/07

River Mile 12.85

Habitat Type: Pool

Notes: None

Dimensions: 6’ wide, 20’ long, 1.0’ deep

Fish Count: 2 adult

Flow: Not measurable

Duncan Creek

surveyed 8/16/07

River Mile 13.3

Upstream extent of trout in Duncan Creek (survey continued 0.3 miles upstream)

Habitat Type: Pool

Notes: None

Dimensions: 8’ wide, 19’ long, 0.75’ deep

Note: Very little habitat upstream, very low surface flow upstream of this point

Fish Count: 3 YOY

Flow: Not measurable

Duncan Creek

surveyed 8/16/07

River Mile 13.6

Habitat Type: Bedrock Sheet

Notes: Upstream extent of survey on Duncan Creek. Flow is only a steep trickle over bedrock and claypan, very little habitat

Dimensions: Not Available

Fish Count: No fish

Flow: Not measurable

TABLES

MAPS