Table AQ 11-13.	Summary of In-situ Measurements for Voluntary Enhanced Water Quality Sampling Locations.

| Sample ID | Location Name | Date | Temperature | Dissolved Oxygen | Specific Conductance | pH | Sample Water Depth1 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (°C) | (mg/L) | (µS/cm at 25 °C) |  | (m) |
| Additional Sampling below Project Reservoirs |
| RR-2A | Rubicon River below Hell Hole Reservoir outlet pipe | 5/22/2007 | 6.88 | 9.0 | 59 | 6.9 | 0 |
| RR-EC | Leakage weir channel below Hell Hole Reservoir | 5/22/2007 | (3) | (3) | (3) | (3) | 0 |
| RR-BEC | Rubicon River below Hell Hole Reservoir and leakage weir channel | 5/22/2007 | 7.13 | 9.8 | 54 | 7.2 | 0 |
| FM-A | Leakage weir A below French Meadows Reservoir | 8/6/2007 | 13.3 | 1.1 | 165 | 5.3 | 0 |
| FM-B | Leakage weir B below French Meadows Reservoir | 8/6/2007 | 11.57 | 5.2 | 180 | 5.6 | 0 |
| FM-C | Leakage weir C below French Meadows Reservoir | 8/6/2007 | 9.65 | 2.9 | 181 | 5.5 | 0 |
| FM-D | Middle Fork American River below French Meadows Reservoir and spillway channel | 8/6/2007 | 4.21 | 9.3 | 26 | 5.3 | 0 |
| FM-E | Middle Fork American River below French Meadows Reservoir outlet pipe | 8/6/2007 | 8.22 | 9.1 | 25 | 5.4 | 0 |

1: Water sample was collected just below the water surface unless otherwise noted.

2: Secchi depth measurements were only collected in reservoirs.

3: Instrument malfunction, no in-situ measurement available.