APPENDIX B

Glossary of Analytical Laboratory Terminology,
Units of Measurements and Calculations

Glossary

Method Detection Limit (MDL):

Is a measure of the method sensitivity. The MDL is the lowest concentration that can be detected by an instrument with correction for the effects of sample matrix and method-specified parameters such as sample preparation. It is the minimum concentration of a substance that can be measured and reported with 99 percent confidence that the analyte concentration is greater than zero, as defined in 40 CFR 136, Appendix B, revised as of July 1, 2003.

Practical Quantitation Limit (PQL):

The concentration that can be reliably measured within specified limits and accuracy during routine laboratory operating conditions. It is typically determined by a combination of the IDL (instrument detection limit-the lowest the instrument is capable of seeing with specified confidence limits) and the lowest calibration standard used. The calibration level is selected (usually greater than the IDL) based upon the needs of the specified batch of samples being run.

Reference Dose (RfD):

The daily exposure of mercury likely to be without significant risk of deleterious health effects during a lifetime.  It is an estimate, with uncertainty spanning perhaps an order of magnitude (Klasing and Brodberg 2006).

Screening Value (SV):

Concentration of mercury in fish or shellfish tissue that are of potential public health concern and that are used as threshold values against which levels of contamination in similar tissue collected from the ambient environment can be compared.  Exceedance of these SVs should be taken as an indication that more intensive site-specific monitoring and/or evaluation of human health risk should be conducted (Cal EPA 2005).

Units of Measure

The following table summarizes common mass ratios for solutions and solids.

| Unit | Solutions | Solids |
| --- | --- | --- |
| ppm (parts per million) 10-6 | mg/L | μg/mL | mg/kg | μg/g |
| ppb (parts per billion) 10-9 | μg/L | ng/mL | μg/kg | ng/g |
| ppt (parts per trillion) 10-12 | ng/L | pg/mL | ng/kg | pg/g |

The following table summarizes the laboratory units and conversions used in the report.

| Water Quality Analytes | Laboratory Given Unit | Water Quality Standard Unit | Conversion to Water Quality Standard Unit |
| --- | --- | --- | --- |
| General Parameters |  |
| Calcium | mg/L | mg/L | No conversion |
| Chloride | mg/L | mg/L | No conversion |
| Hardness (as CaCO3) | mg/L | mg/L | No conversion |
| Magnesium | mg/L | ug/L | Multiply by 1,000 |
| Nitrate/Nitrite (NO3) | mg/L | mg/L | No conversion |
| Ammonia as N | mg/L | mg/L | No conversion |
| Total Kjeldahl Nitrogen (TKN) | mg/L | mg/L | No conversion |
| Total Phosphorus | mg/L | mg/L | No conversion |
| Ortho-phosphate | mg/L | mg/L | No conversion |
| Potassium | mg/L | mg/L | No conversion |
| Sodium | mg/L | mg/L | No conversion |
| Sulfate (SO4) | mg/L | mg/L | No conversion |
| Total Dissolved Solids | mg/L | mg/L | No conversion |
| Total Suspended Solids | mg/L | mg/L | No conversion |
| Turbidity | NTU | NTU | No conversion |
| Organic Carbon, Total (TOC) | mg/L | mg/L | No conversion |
| Total Alkalinity (as CaCO3) | mg/L | mg/L | No conversion |
| Metals-Dissolved |  |
| Arsenic | ug/L | ug/L | No conversion |
| Cadmium | ug/L | ug/L | No conversion |
| Copper | ug/L | mg/L | Divide by 1,000 |
| Iron | ug/L | mg/L | Divide by 1,000 |
| Lead | ug/L | ug/L | No conversion |
| Manganese | ug/L | ug/L | No conversion |
| Nickel | ug/L | ug/L | No conversion |
| Chromium-Total | ug/L | ug/L | No conversion |
| Metals-Total |  |
| Mercury | ng/g | ug/L | Divide by 1,000 |
| Methyl mercury | ng/g fish | mg/Kg fish | Divide by 1,000 |
| Hydrocarbons |  |
| Methyl-tertiary-butyl Ether (MtBE) | ug/L | ug/L | No conversion |
| Total Petroleum Hydrocarbons (as gasoline and as diesel) | ug/L | ug/L | No conversion |
| Oil and Grease | mg/L | mg/L | No conversion |
| Bacteria |  |
| Total Coliform (3x5, 6 hr hold) | MPN/100 mL | MPN/100 mL | No conversion |
| Fecal Coliform (3x5) | MPN/100 mL | MPN/100 mL | No conversion |

Calculations

Several criteria must be calculated on a site-by-site basis. The following equations apply to those analytes.

Ammonia:

Criteria are temperature and pH dependent.

Criteria Continuous Concentration (CCC) with fish early life stages present (mg/L)=

Where T = temperature in degrees C.

Cadmium (Cd):

Criteria are hardness dependent.

California Toxics Rule (CTR) Criteria to Protect Freshwater Aquatic Life:

Criteria Continuous Concentration (CCC) (4-day Average, dissolved, ug/L)=

(exp{0.7852[ln(hardness in mg/L)]-2.715}) x (1.101672- {[ln(hardness in mg/L)] x [0.041838]})

Criteria Maximum Concentration (CMC) (24-hour Average, dissolved, ug/L)=

(exp{1.128[ln(hardness in mg/L)]-3.6867}) x (1.136672- {[ln(hardness in mg/L)] x [0.041838]})

National Toxics Rule (NTR) Criteria to Protect Freshwater Aquatic Life (more stringent):

Criteria Continuous Concentration (CCC) (4-day Average, dissolved, ug/L)=

(exp{0.7409[ln(hardness in mg/L)]-4.719}) x (1.101672- {[ln(hardness in mg/L)] x [0.041838]})

Criteria Maximum Concentration (CMC) (24-hour Average, dissolved, ug/L)=

(exp{1.0166[ln(hardness in mg/L)]-3.924}) x (1.136672- {[ln(hardness in mg/L)] x [0.041838]})

Copper (Cu):

Criteria are hardness dependent.

California Toxics Rule (CTR) Criteria to Protect Freshwater Aquatic Life:

Criteria Continuous Concentration (CCC) (4-day Average, dissolved, mg/L)=

(e{0.8545[ln(hardness in mg/L)]-1.702}) x (0.960)

Criteria Maximum Concentration (CMC) (24-hour Average, dissolved, mg/L)=

(e{0.9422[ln(hardness in mg/L)]-1.700}) x (0.960)

Lead (Pb):

Criteria are hardness dependent.

California Toxics Rule (CTR) Criteria to Protect Freshwater Aquatic Life:

Criteria Continuous Concentration (CCC) (4-day Average, dissolved, ug/L)=

(e{1.273[ln(hardness in mg/L)]-4.705}) x (1.46203- {[ln(hardness in mg/L)] x [0.145712]})

Criteria Maximum Concentration (CMC) (24-hour Average, dissolved, ug/L)=

(e{1.273[ln(hardness in mg/L)]-1.460}) x (1.46203- {[ln(hardness in mg/L)] x [0.145712]})

Nickel (Ni):

Criteria are hardness dependent.

California Toxics Rule (CTR) Criteria to Protect Freshwater Aquatic Life:

Criteria Continuous Concentration (CCC) (4-day Average, dissolved, ug/L)=

(e{0.8460[ln(hardness in mg/L)]+0.0584}) x (0.997)

Criteria Maximum Concentration (CMC) (24-hour Average, dissolved, ug/L)=

(e{0.8460[ln(hardness in mg/L)]+2.255}) x (0.998)