Table REC 4-4.	Pedestrian Stream Crossing Criteria based on Existing Literature and Focus Group Comments.

| Source | Water Depth (feet) | Velocity (ft/sec) | Comments |
| --- | --- | --- | --- |
|  | Preferred | Maximum | Preferred | Maximum |  |
| Recreational Trail Design and Construction (University of Minnesota) | 2.0 | - | Slow moving | - | Article states “Fords (or natural crossings) often can be used to traverse slow moving stream less then 24 inches deep”. |
| Trail Construction and Maintenance Notebook (USDOT a) | 1.3 - 2.0 | - | Low to moderate flow | - | Article states that “A ford for hikers…should be no deeper than 16 to 24 inches (about knee high).” |
| Flow Requirements for Recreation and Wildlife in New Zealand Rivers (Mosley) | 1.3 - 1.9 | 3.9 | 1.64 | (2.2) | Applies to wading. Preferred conditions also apply to “tramping.” Max velocity was derived from depth/velocity figure presented in article and applies to average adults to teenagers (B curve). |
| Methods of Assessing Instream Flows for Recreation (Hyra) | .75 - 2.5 | 4.0 | 0.25 – 2.0 | 3.0 | Applies to water contact wading. Preferred = Hyra’s “optimum”. Max depth and velocity are based on physical criteria, not safety criteria. |
| Focus Group Consultation (Ruck-a-Chucky) | 1.7 | - | - | - | Focus group said target depth is about “knee high (assumed to be 20 inches on average). |
| Focus Group Consultation (Poverty Bar) | 1.5 |  | - | - | Focus group said “max” crossing depth for hikers/runners is 18 inches at Poverty Bar. However, this value was placed in the “preferred” category, because velocities drive wading suitability in this location. |
| Average | 1.9 | 4.0 | 1.8 | 2.6 |  |

Tests:

Preferred Depth x Preferred Velocity = 3.4

Max Depth x Max Velocity = 10.4