Potential Resource Issues:

Stable channel form and fluvial processes.

Project Nexus:

Project operations modify or could potentially modify the flow regime in the bypass and peaking reaches and capture sediment in Project reservoirs and diversion pools, resulting in changes to channel morphology and fluvial processes.

Potential License Condition:

- Channel riparian maintenance flows.

- Sediment Management Plan.

- Pulsed Flows.

- Channel Restoration.

Study Objective(s):

- Document sediment conditions in the bypass reaches and the peaking reach.

- Characterize sediment capture in Project reservoirs and diversion pools under existing Project operations and potential Project betterments operations.

- Develop information to assist in the identification of flows necessary to maintain geomorphic processes in the bypass reaches and the peaking reach.

- Characterize large woody debris capture in reservoirs and diversion pools and document the historical large woody debris management practices.

Extent of Study Area:

The study area will include the bypass reaches, the peaking reach, comparison streams, and Project reservoirs and diversion pools (Table AQ 9-1).

Study Approach:

The following describes the geomorphology study approach which includes data collection and analyses for evaluating (1) sediment conditions in the bypass and peaking reaches, (2) sediment capture in Project reservoirs and diversion pools, (3) flows necessary to maintain geomorphic processes, and (4) large woody debris (LWD) capture and management in reservoirs and diversion pools.

- Initial studies to characterize the geomorphic conditions of the river channels upstream and downstream of Project dams and diversions were completed by PCWA in 2005 and 2006 (PCWA 2005).  This information was collected following methods as described in the 2005-2006 Existing Environment Study Plan Package which is available at the PCWA website: http://relicensing.pcwa.net/.  A technical report summarizing the 2005 data is also available on the website.  The 2006 data will be summarized in a report available in early 2007.  The objectives for these studies are summarized in Table AQ 9-2.

Sediment Conditions in the Bypass and Peaking Reaches

The amount of fine sediment in pools and the particle size composition and fine sediment content of spawning gravels will be determined in the bypass and peaking reaches, as described below.

Fine Sediment in Pools

A quantitative analysis (Hilton and Lisle, 1993) of fine sediment volume in 12 pools in the Middle Fork American and Rubicon rivers above Ralston Afterbay in the fall of 2006 found that the amount of fine sediment was very low; V* values averaged 0.03 (PCWA 2007). V* values less than 0.1 are indicative of low amounts of fine sediment.

- Conduct V* visual estimates in 10 pools at each of 11 sampling locations (Table AQ 9-1) centered on the 2006 geomorphic and riparian quantitative study sites within the bypass reaches, peaking reach, and comparison reaches to characterize the amount of residual pool fine sediment.  Pools with V* values that are relatively low (less than 0.1) can be reasonably approximated by visual estimation (Hilton and Lisle, 1993).  If there are problems completing the V* estimates (for example, due to excessive pool depths or V* values exceed 0.1), then this will be immediately communicated to the Aquatic TWG for further consultation.

  - Due to their very large size and depth (can be over ½-mile long and exceed 10-feet deep), pools on the Middle Fork American River below Ralston Afterbay and on the North Fork American River above Lake Clementine (comparison stream), will require a significantly greater effort to sample.  Therefore, a total of 5 pools, instead of 10, will be visually surveyed on these two stream reaches.

  - Visual estimates of V* will be made using a snorkel and mask, and may require the assistance of divers (due to the excessive pool depth and size) at some locations.  The visual surveys will be supported by photographic documentation of pool bottom sediments, and sketch maps indicating the location and surface area of any fine sediment patches observed.

Particle Size Composition and Fine Sediment Content of Spawning Gravels

- Determine particle size distribution and fine sediment content of spawning gravels at 4 sites in each bypass, peaking, and comparison reach using bulk sampling techniques (McNeil and Ahnell, 1960).  The sites will be selected within or immediately adjacent to the 2006 geomorphic and riparian quantitative sites. These locations are listed in Table AQ 9-1.

  - Collect bulk samples using a modified McNeil sampler (i.e., bottomless bucket) to depths that approximate that of a trout egg pocket in a redd.  Coarse sediments will be sieved and weighed on-site.  Finer sediments will be packaged for transport from the field site and later dried, sieved, and weighed.

  - One “side-by-side” replicate pair of bulk samples will be taken in each of the study sites to provide a measure of the variability in particle size composition within the same gravel deposit to characterize an expected range of natural variability.

- Plot particle size composition of spawning gravel samples as cumulative distribution curves and histograms.  Statistically analyze the particle size composition as represented by the D50, D16, and D84.

- Compare particle size composition and fine sediment content to standards from the scientific literature (Kondolf, 1988 and 2000) and, where applicable, to the relevant comparison streams.

Sediment Capture in Project Reservoirs and Diversion Pools

The capture of sediment in Project reservoirs and diversion pools will be evaluated based on a review of existing sediment management information and data collected from field studies as described below.

Obtain Sediment Management Information

- Obtain information on sediment management practices implemented at Project diversion pools.

  - Summarize existing sediment management conducted by PCWA Operations and Maintenance personnel.

  - Obtain historic information, as available, pertaining to volume of sediments excavated and frequency of maintenance, for each facility.

  - Summarize any historical and recent bathymetry data and studies on Project reservoirs and diversion pools noting change in sediment accumulation over time.

Determine Particle Size Composition and Estimate Sediment Loads Captured at Project Reservoirs and Diversion Pools

- Survey French Meadows and Hell Hole reservoirs, Ralston Afterbay and Middle Fork Interbay, during low-pool conditions to quantify and characterize sediment capture.

  - Estimate the proportion in-filled with sediments by a combination of topographic surveys using an automatic level, and visual survey over the exposed reservoir bed above the low-pool if bathymetry surveys are not available.

  - Identify and photograph any evidence indicating the location of the original, pre-dam valley/river bottom conditions, such as tree-stumps.

- Conduct pebble counts (Wolman 1954) for surface sediments and bulk sampling for subsurface sediments to determine particle sizes captured and removed.  Sampling will occur during either dry or low-pool conditions at each Project reservoir and diversion pools.

  - Perform sampling in representative areas of each reservoir that is dry and accessible during low-pool. The number of sampling points will depend upon the size of the area with visible deposition, and the relative heterogeneity of the deposition.  Heterogeneous sampling areas will be visually delineated into relatively homogeneous units (e.g., sand, gravel, cobble, boulder), and particle size sampling will take place in each defined unit.

  - Subsurface bulk sampling will be performed using hand tools to dig below ground surface.  A shovel or hand-auger will be used to obtain vertically-integrated depth samples.  It is expected that bulk samples will be taken up to approximately 2 feet below ground surface, although a core sample with a hand auger could sample up to 10 ft depths if the subsurface material is no larger than fine gravels (about 16mm).

  - Visually catalogue all bulk samples for particle size (i.e., proportion of sediments in silt, sand, gravel, cobble size ranges), and photo-document.  One-half of the catalogued bulk samples will be retained for sieving and particle size analysis.  For the larger reservoirs, collect and catalogue about 24 samples, with about 12 samples retained for particle size analysis.

  - Bulk sampling of sediments in the South Fork Long Canyon and North Fork Long Canyon diversion pools was performed in September 2006, just prior to planned maintenance activities at these locations.  If these diversion pools re-fill with sediment in 2007 or 2008, then they will be re-sampled and particle sizes compared with those obtained from the bulk samples in 2006.

  - Sketch maps of the surface particle size composition of the visible beds of the reservoir and diversion pool beds.  The surficial area of any visible gravel deposits will be measured and recorded on the sketch maps.

  - In addition to the bulk samples collected by hand tools, a backhoe will be used at French Meadows Reservoir and at Duncan Creek diversion to dig test pits at depths up to approximately 8 feet (assuming that groundwater does not interfere with sampling).   The material at depth in the pits will be visually catalogued, photographed, and one sub-sample from each test pit will be retained for sieving and particle size analysis.  The test pits will be used to determine if there is any vertical sorting of particle sizes at depth and whether or not the samples obtained by hand tools from shallower depths accurately represent the range of particle sizes deposited at depth in the reservoir.

Identify Flows Necessary to Maintain Geomorphic Processes in Bypass Reaches and the Peaking Reach

Information regarding flows that are necessary to maintain geomorphic processes in the bypass reaches and peaking reach will be developed by comparing impaired and unimpaired hydrologic regimes and evaluating sediment transport conditions under different flow regimes in the bypass and peaking reaches, as outlined below.

Compare Impaired and Unimpaired Hydrologic Regimes

- Compare impaired and unimpaired hydrologic regimes (high flow magnitude, duration, and frequency) in bypass reaches and the peaking reach using methods outlined in Guidelines for determining flood flow frequency: Bulletin 17B of the Hydrology Subcommittee, Interagency Advisory Committee on Water Data (USGS 1982) and Flood Frequency Analyses, Manual of Hydrology (Dalrymple 1960).

  - Determine unimpaired flood flow frequency from existing gaging records where available, as follows:

    - 11433500 Middle Fk American Nr Auburn (1912-1964, pre-dam era)

    - 11431000  Rubicon River Nr Georgetown (1943-1964, pre-dam era)

    - 11427700 Duncan Ck Nr French Meadows (1965-2005)

  - Evaluate the applicability of existing regional flood frequency curves (USGS 1993) based on the above referenced unimpaired flow data.  If necessary, develop a regional flood frequency curve using the analytical procedures outlined by the USGS (Dalrymple, 1960) to determine the magnitude and frequency of unimpaired flows for ungaged locations, or locations with insufficient gaging records.  The regional flood frequency analysis uses unimpaired flow records from gaging stations within the same hydro-physiographic region as the Middle Fork American River.  Climatic trends, if any are identified, will be considered as may be necessary when selecting the appropriate hydrologic data set for flood frequency analysis.

    - Evaluate potential candidate unimpaired gaging stations for consideration in developing the regional unimpaired flood frequency curve in consultation with the Aquatic Technical Working Group (TWG).  The potential candidate unimpaired gaging stations for consideration are listed in Table AQ 9-3.

Evaluate Sediment Transport Conditions under Different Flow Regimes at Selected Quantitative Study Sites

- Identify sediment transport flows at the geomorphic and riparian quantitative transects and instream flow transects using the hydraulic models developed for the AQ 1 –Instream Flow Technical Study.

  - Collect stage-discharge data at high flows at geomorphic and riparian transects in select reaches to calibrate the hydraulic model.

    - For purposes of the sediment transport assessment, the range of flows used for stage-discharge calibration will be extended into higher discharges than typically required for aquatic habitat instream flow modeling.   Stage data (i.e., water surface elevations) will be collected either by field observations during high flows (e.g., flagging water surface elevation on the banks, or from pre-installed staff gages) or by installation of automated pressure transducers that provide continuous water depth measurements.

  - Coordinate hydraulic modeling for sediment transport with the AQ 1 – Instream Flow Technical Study.  The sediment transport modeling will be based on the hydraulic modeling described in the AQ 1 – Instream Flow Study.  The same study sites on the bypass and peaking reaches proposed for the AQ 1 – Instream Flow Technical  Study will be evaluated for sediment transport conditions in this study (Table AQ 9-1).

  - Derive channel geometry data for input to the models from the cross-section and longitudinal topographic surveys performed as part of the AQ 1 – Instream Flow Technical Study.

    - Channel geometry data shall include identification of the bankfull flow elevation (bankfull elevation has already been identified for any transects that may be used from the 2006 geomorphology Level II field studies).  The discharge corresponding to the bankfull elevation will be determined from the instream flow model simulations.

  - Derive channel hydraulic conditions, including flow depth, velocity, energy slope, and bed shear stress, from the models for a range of high flows.

    - Bed shear stress, which is calculated as a depth-slope product, will be obtained as an output from the AQ 1 – Instream Flow Study modeling.  Bed shear stress (τ) will be expressed as an average force (lbs/sq. ft.) over the transect width.

    - Determine the shear stress required to initiate motion for a given particle size from the Shield’s criterion that defines the critical shear stress ((*ci, the shear stress threshold at which incipient motion occurs).  The bed shear stress obtained from the model and the Shield’s criterion will be used to determine the particle sizes that are mobilized over the range of flows.  Shield’s relationship for critical shear stress is defined as, ( *ci = ( ((s - (  ) d50. Where: ( = Shield’s parameter (a dimensionless variable), (, (s = specific weight of the fluid and sediment, respectively, and d50  =  median particle diameter.

    - A range of commonly accepted values from the geomorphic and engineering literature will be documented and used for Shield’s parameter (().  A range of critical shear stress and corresponding range of discharge values at which initiation of motion occurs for a given particle size will be presented.

  - Determine particle sizes in the channel from pebble counts performed for the Rosgen Level II channel classification, and/or bulk sediment samples, or from data collected as part of the Instream Flow Technical Study.

- In consultation with the Aquatic TWG, determine if additional empirical studies are necessary to characterize sediment transport under different flow regimes.  If warranted the specific empirical studies to be applied at each study site will be dependent upon the specific study objective and the site specific characteristics.  If empirical studies are warranted develop the scope of the studies in consultation with the Aquatic TWG.  The study methods are likely to include one or a combination of the following approaches.

  - Placement and monitoring of tracer gravels

  - Installation and monitoring of pit traps

  - Installation and monitoring of scour chains

- Apply the procedure outlined in Grant et al. (2003) for predicting the geomorphic response of project rivers and streams to Project dams, including developing a graph  that shows the response domain for predicted channel adjustments in relation to T* and S*.

Large Woody Debris Capture and Management in Reservoirs and Diversion Pools

The amount of LWD captured in Project reservoirs and diversion pools, and the relative extent to which large woody debris capture may effect the recruitment of LWD in downstream reaches will be characterized, as follows:

- Describe historical and existing large woody debris management by PCWA.

- Survey and quantify large woody debris captured at Project reservoirs and diversion pools.

- Characterize the fate of large woody debris transport into Project reservoirs and diversion pools using a combination of field observations, Project records, operator interviews, and historical water level records.

- Compare LWD amounts and function in bypass and peaking reaches above and below reservoirs and diversion pools.  This information was collected as part of the Aquatic Habitat Characterization Study conducted by PCWA in 2006 (PCWA In progress).

Schedule:

| Date | Activity |
| --- | --- |
| July through December 2007 | Conduct sediment survey and hydrology analysis |
| January and February 2008 | Complete data analysis |
| March through June 2008 | Conduct sediment transport field surveys in coordination with instream flow surveys |
| July through September 2008 | Analyze data and prepare draft report |
| October 2008 | Distribute draft report to the Aquatic TWG |
| October and November 2008 | Aquatic TWG 60 day review and comment period |
| December 2008 | Aquatic TWG consultation (need for additional empirical studies) |
| January and February 2009 | Resolve comments and prepare final report |
| March 2009 | Distribute final report to the Aquatic TWG and Plenary |
| April 2009 through January 2010 | Conduct contingency geomorphology related studies, data analysis and report production |

Level of Effort and Cost:

To be determined.

References:

Dalrymple, Tate.  1960.  Flood frequency analyses, Manual of Hydrology: Part 3.  U.S. Geological Survey Water Supply Paper 1543-A.

Grant, Gordon E., John C. Schmidt, and Sarah L. Lewis, 2003.  A geologic framework for interpreting downstream effects of dams on rivers.  AGU, Water Science and Application 7, Geology and Geomorphology of the Deschutes River, Oregon.

Hilton, Sue, and Thomas E. Lisle, 1993.  Measuring the fraction of pool volume filled with fine sediment.  Res. Note PSW-RN-414.  Albany, CA:  Pacific Southwest Research Station, Forest Service, U.S. Department of Agriculture.

Kondolf, G.M.  1988.  Salmonid spawning gravels:  A geomorphic perspective on their size distribution, modification by spawning fish, and criteria for gravel quality.  PhD thesis.  Johns Hopkins University, Baltimore.

Kondolf, G.M.  2000.  Assessing salmonid spawning gravel quality.  Transactions American Fisheries Society, 129: 262-281.

McNeil, W.J. and W.H. Ahnell.  1960.  Measurement of gravel composition of salmon stream beds.  University of Washington Fish. Res. Inst. Circ. No.120.

Placer County Water Agency (PCWA).  2005.  Middle Fork American River Project (FERC 2079).  2005-2006 Existing Environment Study Plan Package. June 17, 2005.

PCWA.  (2007). Middle Fork American River Project (FERC 2079) 2006 Draft Physical Habitat Characterization Study.  April, 2007.

U.S. Geological Survey (USGS).  1982.  Guidelines for Determining Flood Flow Frequency:  Bulletin 17B of the Hydrology Subcommittee, Interagency Advisory Committee on Water Data.

USGS.  1993.  Nationwide summary of U.S. Geological Survey regional regression equations for estimating magnitude and frequency for ungaged sites.  Water-Resources Investigations Report 94-4002.

Wolman, M.G.  1954.  A method of sampling coarse bed material. American Geophysical Union, Transactions, 35: 951-956.

AQ 9-1.	V*, Bulk Spawning Gravel, and Sediment Transport Hydraulic Model Locations.

| River/Reach | Bypassed Reach | Peaking Reach | Initiation of Motion Sediment Transport Modeling Sites | Number of bulk spawning gravel samples | Number of V* pools |
| --- | --- | --- | --- | --- | --- |
| Duncan Creek |  |  |  |  |  |
| Duncan Creek | ( |  | 1 | 4 | 10 |
| Middle Fork American River (MFAR) |  |  |  |  |  |
| MFAR French Meadows – Interbay | ( |  | 1 | 4 | 101 |
| MFAR Interbay – Ralston | ( |  | 1 | 4 | 102 |
| MFAR Below Ralston |  | ( | 1-2 | 4 | 5 |
| Rubicon River |  |  |  |  |  |
| Rubicon River Hell Hole – South Fork | ( |  | 1 | 4 | 10 |
| Rubicon River South Fork – Ralston | ( |  | 2 | 4 | 103 |
| Long Canyon Creek |  |  |  |  |  |
| North Fk Long Canyon | ( |  | 1 | 4 | 10 |
| South Fk Long Canyon | ( |  | 1 | 4 | 10 |
| Long Canyon | ( |  | 1 | 4 | 10 |
| Comparison Streams |  |  |  |  |  |
| North Fk Middle Fk American |  |  |  | 4 | 104 |
| North Fk American |  |  |  | 4 | 5 |

1Note: Two pools were surveyed in 2006, therefore only 8 additional pools will be surveyed in 2007.

2Note: Six pools were surveyed in 2006, therefore only 4 additional pool will be surveyed in 2007.

3Note: One pool was surveyed in 2006, therefore only 9 additional pools will be surveyed in 2007.

4Note: Three pools were surveyed in 2006, therefore only 7 additional pools will be surveyed in 2007.

Table AQ 9-2.	2005 and 2006 Geomorphology Study Objectives.

2005 and 2006 Geomorphology Purpose

Characterize geomorphic conditions of the river channel upstream and downstream of Project dams and diversions.

2005 and 2006 Study Plan Objectives

Classify and organize bypass reaches into distinct reaches based on stream morphology.

Distinguish the relative responsiveness (i.e., “sensitivity”) of river reaches to alterations of flow and sediment regimes.

Describe geomorphic conditions of river reaches immediately upstream of Project facilities to evaluate their suitability to serve as reference reaches in later study phases.

Identify potential comparison streams (reference reaches) in the vicinity of the MFP if reaches immediately upstream of Project facilities are determined to be unsuitable as reference reaches.

Provide framework for organizing future survey efforts.

Table AQ 9-3.	Potential Candidate Unimpaired Gaging Stations for Consideration in Development of Regional Unimpaired Flood Frequency Curve.

| USGS Gage Number | Gaging Station Name | Period of Record |
| --- | --- | --- |
| 11433400 | Canyon Ck Nr Georgetown | 1966-1979 |
| 11432500 | Pilot Ck Nr Georgetown | 1947-1960 |
| 11431800 | Pilot Ck Abv Stumpy Meadows Res | 1960-2005 |
| 11430000 | So Fk Rubicon R Bl Gerle Ck Nr Georgetown | 1911-2005 |
| 11426150 | Onion Ck Nr Soda Springs | 1961-1979 |
| 11428000 | Rubicon R A Rubicon Springs Nr Meeks Bay | 1955-1996 |
| 11426200 | NF Forbes Ck Nr Dutch Flat | 1955-1985 |
| 11426400 | N Shirttail Ck Nr Dutch Flat | 1955-1984 |
| 11426500 | NF American River Nr Colfax | 1912-1941 |
| 14270000 | NF American River Abv North Fk Dam | 1942-2005 |
| 11433260 | NF of MF American R Nr Foresthill | 1966-1984 |
| 11434000 | NF American River A Rattlesnake Bar | 1931-1955 |
| 11433500 | Middle Fk American Nr Auburn | 1912-1964, pre-dam era |
| 11431000 | Rubicon River Nr Georgetown | 1943-1964, pre-dam era |