Table AQ 7-1. Middle Fork Project Facilities – Entrainment Characteristics

| Facility | Hydraulic Capacity (cfs) | Frequency of Use (cfs) | Inlet/Outlet Type | Inlet Area (ft.2) | Approach Velocity (fps) | Intake Depth (ft) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- |
| French Meadows Reservoir |
| French Meadows-Hell Hole Tunnel | Existing Project: 400 Betterment: 800 | Frequent during spring and summer | Inlet: 10 ft. dia. pipe. Trash rack with 2.6 in. bar spacing. Outlet: vertical Francis turbine | Inlet: 78.5 Trash Rack: 484 | Inlet/Exist: 0-5.1 Inlet/Better: 0-10.2 Trash Rack/Exist: 0-0.8 Trash Rack/Better: 0-1.6 | 145(1) | Betterment – French Meadows Powerhouse capacity upgrade. French Meadows Powerhouse discharges into Hell Hole Reservoir. |
| French Meadows Dam – Low Level Outlet | 1,430 | Infrequent | Inlet: 60 in. pipe with slide gate. Trash rack with 6 in. bar spacing. Outlet: 60 in. Ring Jet Valve | Inlet: 28 Trash Rack: 52 | Inlet: 0-51 Trash Rack: 0 - 28 | 211.5(2) | Energy dissipating valve discharges to a plunge pool |
| French Meadows Dam – Instream Flow Pipe Intake | 4 - 8 | Continuous | Inlet: 8 in. pipe. Outlet: 8 in. Howell-Bunger Valve | Inlet: 0.35 Trash Rack: 23 | Inlet: 11.4 – 22.86 Trash Rack: 0.2 – 0.4 | 194(1) | Energy dissipating valve discharges to a plunge pool |

(1)Maximum reservoir operating surface elevation minus intake surface elevation.

(2) Maximum reservoir operating surface elevation minus curb intake elevation.

Table AQ 7-1. Middle Fork Project Facilities – Entrainment Characteristics (cont.).

| Facility | Hydraulic Capacity (cfs) | Frequency of Use (cfs) | Inlet/Outlet Type | Inlet Area (ft.2) | Approach Velocity (fps) | Intake Depth (ft) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Hell Hole Reservoir |
| Hell Hole-Middle Fork Tunnel | 800 | Frequent | Inlet: 11.5 ft. dia. pipe. Trash rack with 2 in. bar spacing Outlet: Two Pelton Turbines | Inlet: 104 Trash Rack: 705 | Inlet: 0-7.8 Trash Rack: 0-1.1 | 308.1(1) | Powerhouse discharges into Middle Fork Interbay |
| Hell Hole Dam Outlet Works | 6-848 | Continuous low flow (6-20); Infrequent during outages (approx. 65); Infrequent and would cause facility damage (65-848) | Rectangular inlet (with trash rack) into horizontal 13 ft. horseshoe shaped tunnel (original tunnel opening shut with stop logs). | Inlet: 76 Trash Rack: 300.3 | Inlet: 0.08-11.2 Trash Rack: 0.02-2.82 | 342(2) | Outlet works is a tunnel that leads to a 48 in. dia. pipe and 16 in. dia. pipe for the Hell Hole Powerhouse, instream flow pipe, and low level outlet. |
| Hell Hole Dam Low Level Outlet(4) | Calculated maximum capacity 848 | Infrequent (would cause facility damage) | Inlet: 48 in. dia. pipe with butterfly valve. Outlet: 48 in. hollow-cone valve | 12.6 | 48 in. pipe opening inlet: 0-67.3(3) | 342(2) | Energy dissipating valve discharges to a plunge pool |
| Hell Hole Power House(4) | Approx 45 | Continuous except for maintenance | Inlet: 20 in. dia. pipe with control valve Outlet: horizontal Francis turbine | 2.18 | 20 in. pipe opening inlet: 0-20.6(3) | 342(2) | 20 in. dia. penstock for powerhouse “Y’s” off of 48 in. dia pipe. Hell Hole Powerhouse discharges to plunge pool |
| Hell Hole Dam Instream Flow Pipe(4) | 20 | Infrequent (typically Instream flow compliance is provided by Hell Hole Powerhouse) discharge | Inlet: 16 in. dia. pipe with butterfly valve. Outlet: 12 in. hollow-cone valve. | 0.8 | 16 in. pipe opening inlet: 0-25(3) | 342(2) | Energy dissipating valve discharges to a plunge pool |

(1) Maximum reservoir operating surface elevation minus intake surface elevation.

(2) Maximum reservoir operating surface elevation minus intake elevation invert of Hell Hole Dam Outlet Works.

(3) Intake velocity calculated at the pipe inlet inside the tunnel.  Intake velocity to the tunnel is much lower (see Hell Hole-Middle Fork Tunnel Intake)

(4) Outlet branches off from tunnel.  Inlet to tunnel is the Hell Hole Dam Outlet Works.

Table AQ 7-1. Middle Fork Project Facilities – Entrainment Characteristics (cont.).

| Facility | Hydraulic Capacity (cfs) | Frequency of Use (cfs) | Inlet/Outlet Type | Inlet Area (ft.2) | Approach Velocity (fps) | Intake Depth (ft) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Middle Fork Interbay |
| Middle Fork – Ralston Tunnel | 836 | Frequent | Inlet: Tunnel with slide gate and trash rack with 3 in.bar spacing Outlet: Pelton Turbine | Tunnel Inlet: 96 Trash Rack: 680 | Inlet: 0-8.71 Trash Rack: 0-1.23 | 51(1) | Ralston Powerhouse discharges into Ralston Afterbay |
| Middle Fork Interbay Dam Low Level Outlet | 895 | Infrequent | Inlet: 60 in. dia. with slide gate and Grizzly (8 in. bar opening) Outlet: Open pipe | Pipe Inlet: 19.6 Grizzly: 62 | Inlet: 0-45.7 Trash Rack: 0-14.4 | 68.5(1) | Discharges to a plunge pool |
| Middle Fork Interbay Dam Stream Maintenance Pipe | 12-23 | Continuous | Inlet: 20 in dia. pipe with slide valve and trash rack (3 in. bar opening) Outlet: Open pipe | Pipe Inlet: 2.18 Trash Rack: 6.0 | Inlet: 5.5-10.6 Trash Rack: 2.0-3.8 | 39.84(1) | Outlet discharges to a plunge pool |

(1) Maximum reservoir operating surface elevation minus intake elevation invert.

Table AQ 7-1. Middle Fork Project Facilities – Entrainment Characteristics (cont.).

| Facility | Hydraulic Capacity (cfs) | Frequency of Use (cfs) | Inlet/Outlet Type | Inlet Area (ft.2) | Approach Velocity (fps) | Intake Depth (ft) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ralston Afterbay |
| Ralston – Oxbow Tunnel | 1,088 | Frequent | Inlet: Tunnel with slide gate and trash rack with 3 in. bar spacing Outlet: vertical Francis turbine | Tunnel Inlet: 96 Trash Rack: 590 | Inlet: 0-11.3 Trash Rack: 0-1.8 | 39(1) | Oxbow Powerhouse discharges into the Middle Fork American River |
| Ralston Afterbay Dam Low Level Outlet | 1,671 | Infrequent | Inlet: 72 in. dia. with slide valve and Grizzly (8” bar opening) Outlet: 72 in. dia. slide gate | Pipe Inlet: 28.3 Grizzly: 82.6 | Inlet: 0-59.1 Trash Rack: 0-20.33 | 74(1) | Discharges to a plunge pool |
| Ralston Afterbay Dam Stream Maintenance Pipe | 75 | Frequent – 10 cfs Infrequent – 75 cfs | Inlet: 30 in. dia. pipe with slide valve and trash rack (3.88 in. bar opening) Outlet: 30 in. dia. Ring Jet valve | Pipe Inlet: 4.9 Trash Rack: 36.2 | Inlet: 2.04-15.31 Trash Rack: 0.3-2.1 | 41.25(1) | Energy dissipating valve discharges to a plunge pool |

(1) Maximum reservoir operating surface elevation minus intake elevation invert.

Table AQ 7-1. Middle Fork Project Facilities – Entrainment Characteristics (cont.).

| Facility | Hydraulic Capacity (cfs) | Frequency of Use (cfs) | Inlet/Outlet Type | Inlet Area (ft.2) | Approach Velocity (fps) | Intake Depth (ft) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Duncan Creek Diversion |
| Duncan Creek – Middle Fork Tunnel | 400 | Frequent | Inlet: Tunnel with stop logs. Trash Rack (with 9 in. bar spacing.) Outlet: Open tunnel | Tunnel Inlet: 51 Trash Rack: 51 | Inlet: 0-7.84 Trash Rack: 0-7.84 | 4.25(1) | Discharges into French Meadows Reservoir |
| Duncan Creek Low Level Outlet | 304 | Infrequent | Inlet: 60 in. dia. pipe w/ slide gate and grizzly with 10 in. bar spacing. Outlet: Open pipe | Pipe Inlet: 19.6 Grizzly: 58.7 | Inlet: 0-15.5 Trash Rack: 0-5.2 | 13.5(2) | Discharges to a plunge pool |
| Duncan Creek Stream Maintenance Pipe | 4 - 8 | Continuous | Inlet: 10 in. dia. pipe with slide gate and trash screen (with 1.75 in. openings) Outlet: Discharge weir. | Pipe Inlet: 0.55 Trash Screen: 12.2 | Inlet: 7.3-14.6 Trash Rack: 0.33-0.66 | 5(1) | Outlet discharges to a plunge pool |

(1) Diversion Dam Crest minus top of intake weir.

(2) Diversion Dam Crest minus invert elevation.

Table AQ 7-1. Middle Fork Project Facilities – Entrainment Characteristics (cont.).

| Facility | Hydraulic Capacity (cfs) | Frequency of Use (cfs) | Inlet/Outlet Type | Inlet Area (ft.2) | Approach Velocity (fps) | Intake Depth (ft) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- |
| North Fork Long Canyon |
| North Fork Long Canyon Diversion Pipe | 100 | Frequently during winter and spring. No diversion after July 1. | Inlet: Parshall Flume with slide gate to a 36 in. dia pipe. Trash rack w/ 2 in. bar spacing. Outlet: 403 foot deep drop inlet to the Hell Hole - Middle Fork Tunnel | Inlet: 16 Trash Rack: 68.7 | Inlet: 0 – 6.25 Trash Rack: 0 – 1.46 | 6(1) | Discharge to Hell Hole – Middle Fork Tunnel |
| North Fork Long Canyon Low Level Outlet | 104 | Infrequent | Inlet: 36 in. dia. pipe with slide gate Outlet: open pipe | Inlet: 7.1 | Inlet: 0 – 14.7 | 5.5(1) | Discharge to streambed |
| North Fork Long Canyon Stream Maintenance Pipe | 0 - 2 | Continuous | Inlet: 12 in. dia pipe with 12 in. Slide valve Outlet: 25 in. wide concrete channel with weir | Inlet: 0.8 | Inlet: 0 - 2.5 | 6(1) | Discharge to streambed |

(1)  Diversion dam spillway crest minus invert elevation.

Table AQ 7-1. Middle Fork Project Facilities – Entrainment Characteristics (cont.).

| Facility | Hydraulic Capacity (cfs) | Frequency of Use (cfs) | Inlet/Outlet Type | Inlet Area (ft.2) | Approach Velocity (fps) | Intake Depth (ft) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- |
| South Fork Long Canyon |
| South Fork Long Canyon Diversion Pipe | 200 | Frequently during winter and spring. No diversion after July 1 | Inlet: 42 in. dia. pipe with inlet weir. Trash rack w/2.4 in. bar spacing. Outlet: 387 foot deep drop inlet to Hell Hole-Middle Fork Tunnel | Inlet: 36 Trash Rack: 107 | Inlet: 0 – 5.6 Trash Rack: 0 – 1.87 | 11(1) | Discharge to Hell Hole – Middle Fork Tunnel |
| South Fork Long Canyon Low Level Outlet | 136 136 | Infrequent | Inlet: 36 in. dia. pipe with slide gate Outlet: open pipe | Inlet: 7.1 | Inlet: 0 – 19.5 | 12.2(1) | Discharge to streambed |
| South Fork Long Canyon Stream Maintenance Pipe | 2.5 - 5 | Continuous | Inlet: 12 in. dia pipe with 12 in. Slide valve Outlet: 48 in. wide concrete channel with weir | Inlet: 0.8 | Inlet: 3.1 – 6.25 | 6(1) | Discharge to streambed |

(1)  Diversion dam spillway crest minus invert elevation.