| Table SD B-3. Project Facility Specifications. |
| --- |
| DUNCAN CREEK DIVERSION |
| DAM |  |
| Type | Gravity |
| Material | Concrete |
| Height of Dam Crest above Streambed | 32 ft |
| Dam Crest Length | 165 ft |
| Volume | 1,750 cubic yards |
| Elevation of Dam Crest | 5,275 ft |
| Elevation of Streambed | 5,243 ft |
| Elevation of Spillway Crest | 5,265 ft |
| Stream Maintenance Pipe Capacity | 8 cfs |
| SPILLWAY |  |
| Type | Uncontrolled Overflow |
| Width | 100 ft |
| Capacity | 7,200 cfs |
| RESERVOIR |  |
| Gross Storage | 20 ac-ft |
| DUNCAN CREEK – MIDDLE FORK TUNNEL |
| Nominal Size / Shape | 9 ft x10 ft / Horseshoe |
| Length: |  |
| Total | 7,864 ft or 1.5 miles |
| Concrete Lined (Est.) | 300 ft |
| Maximum Diversion Capacity | 400 cfs |
| Invert Gradient | 0.0029 |
| FRENCH MEADOWS DAM (LL ANDERSON DAM) AND FRENCH MEADOWS RESERVOIR |
| DAM |  |
| Type | Composite |
| Material | Rock and Gravel Fill |
| Height of Dam Crest above Streambed | 231 ft |
| Dam Crest Length | 2,700 ft |
| Dam Crest Width | 32 ft |
| Elevation of Dam Crest | 5,273 ft |
| Elevation of Streambed | 5,040 ft |
| Elevation of Spillway Crest | 5,244.5 ft |
| Volume | 3,510,000 cubic yards |
| Slopes – Upstream | 2:1 |
| Slopes – Downstream | 1.8:1 and 2.0:1 |
| Stream Maintenance Pipe Capacity | 8 cfs |
| Maximum Low Level Outlet Capacity at Water Surface 5262 (full reservoir) | 1,430 cfs |
| SPILLWAY |  |
| Type | Gated Ogee Crest |
| Type of Gates | Radial |
| Number of Gates | 2 |
| Size of Gates | 20 ft x 18.5 ft |
| Capacity (Res. Water Surface 5271.0, 2’ freeboard) | 19,800 cfs |
| RESERVOIR |  |
| Maximum Operating Water Surface | 5,262.0 ft |
| Minimum Operating Water Surface | 5,125 ft |
| Gross Storage | 134,993 ac-ft |

| Table SD B-3. Project Facility Specifications (continued). |
| --- |
| DUNCAN CREEK DIVERSION |
| FRENCH MEADOWS DAM (LL ANDERSON DAM) AND FRENCH MEADOWS RESERVOIR (continued) |
| RESERVOIR (continued) |  |
| Dead Storage (as constructed), at Tunnel Intake lip | 7,635 ac-ft |
| Active Storage (as constructed) | 127,358 ac-ft |
| Area at Maximum Operating Water Surface | 1,408 acres |
| Area at Minimum Operating Water Surface | 434 acres |
| Depth at Minimum Operating Water Surface | 77 ft |
| Shoreline at Maximum Operating Water Surface | 9 miles |
| FRENCH MEADOWS — HELL HOLE TUNNEL |
| Nominal Size / Shape | 12 ft 4 in / Horseshoe |
| Length: |  |
| Total | 13,694 ft or 2.6 miles |
| Concrete Lined (Est.) | 1,617 ft |
| Steel Lined (Est.) | 317 ft |
| Maximum Discharge | 400 cfs |
| Invert Gradient | 0.0025 |
| FRENCH MEADOWS POWERHOUSE |
| PENSTOCK |  |
| Length | 691 ft or 0.1 miles |
| Diameter | 6 ft 3 in O.D. |
| POWER PLANT |  |
| Installed Capacity, Generator | 15.3 MW |
| Type of Turbine | Francis |
| Maximum Tail Water Surface | 4,630 ft |
| Minimum Tail Water Surface | 4,608 ft |
| Maximum Static Head | 654 ft |
| Minimum Static Head | 517 ft |
| Elevation Runner | 4,612 ft |
| R.P.M. | 450 |
| HELL HOLE DAM AND RESERVOIR |
| DAM |  |
| Type | Rockfill |
| Height of Dam Crest above Streambed | 410 ft |
| Dam Crest Length | 1,570 ft |
| Dam Crest Width | 35 ft |
| Elevation of Dam Crest | 4,650 ft |
| Elevation of Streambed | 4,240 ft |
| Volume | 8,440,000 cubic yards |
| Slopes - Upstream | 2.5:1 |
| Slopes - Downstream | 1.4:1 |
| Stream Maintenance Pipe Capacity | 20 cfs |
| Maximum Low Level Outlet Capacity at water surface 4,630 (full reservoir) | 852 cfs |
| HELL HOLE DAM AND RESERVOIR (continued) |
| SPILLWAY |  |
| Type | Uncontrolled |
| Elevation of Spillway Crest | 4,630 ft |
| Width at Lip | 350 ft |
| Capacity (Water Surface 4647.1, 2.8’ freeboard) | 89,500 cfs |
| RESERVOIR |  |
| Maximum Operating Water Surface | 4,630 ft |
| Minimum Operating Water Surface | 4,340 ft |
| Gross Storage | 207,590 ac-ft |
| Dead Storage (as constructed), at Tunnel Intake lip | 2,533 ac-ft |
| Active Storage (as constructed) | 205,057 ac-ft |
| Area at Maximum Operating Water Surface | 1,253 acres |
| Area at Minimum Operating Water Surface | 185 acres |
| Depth at Minimum Operating Water Surface | 88 ft |
| Shoreline at Maximum Operating Water Surface | 11 miles |
| HELL HOLE POWERHOUSE |
| Installed Capacity, Generator | 0.73 MW |
| Normal Operating Tail Water Surface | 4,240 ft |
| Maximum Static Head | 391 ft |
| Minimum Static Head | 101 ft |
| R.P.M. | 1,200 |
| HELL HOLE — MIDDLE FORK TUNNEL |
| Nominal Size / Shape | 13 ft 5 in / Horseshoe |
| Length |  |
| Total | 55,006 ft or 10.4 miles |
| Concrete Lined (Est.) | 6,780 ft |
| Steel Lined (Est.) | 5,180 ft |
| Nominal Maximum Discharge, at full reservoir | 920 cfs |
| Invert Gradient | 0.0035 and 0.0077 |
| NORTH FORK LONG CANYON DIVERSION |
| DAM |  |
| Type | Gravity |
| Material | Concrete |
| Height of Dam above Streambed | 10 ft |
| Dam Crest Length | 120 ft |
| Elevation of Dam Crest | 4,720 ft |
| Elevation of Streambed | 4,710 ft |
| Volume | 636 cubic yards |
| Stream Maintenance Pipe Capacity | 2 cfs |
| SPILLWAY |  |
| Type | Uncontrolled Overflow |
| Elevation of Spillway Crest | 4,716 ft |
| Width of Spillway Crest | 95 ft |
| Capacity | 3,000 cfs |
| NORTH FORK LONG CANYON DIVERSION PIPE AND DROP INLET |
| PIPE |  |
| Diameter | 36 in. |
| Length | 3,530 ft or 0.7 miles |
| NORTH FORK LONG CANYON DIVERSION PIPE AND DROP INLET (continued) |
| SHAFT |  |
| Diameter | 6 ft |
| Depth without 6 ft x 20 ft Standpipe | 403 ft |
| Capacity | 100 cfs |
| Invert Gradient | Vertical |
| SOUTH FORK LONG CANYON DIVERSION |
| DAM |  |
| Type | Gravity |
| Material | Concrete |
| Height of Dam Crest above Streambed | 27 ft |
| Dam Crest Length | 145 ft |
| Elevation of Dam Crest | 4,650 ft |
| Elevation of Streambed | 4,623 ft |
| Volume | 1,341 cubic yards |
| Stream Maintenance Pipe Capacity | 5 cfs |
| SPILLWAY |  |
| Type | Uncontrolled Overflow |
| Width of Spillway Crest | 60 ft |
| Elevation of Spillway Crest | 4,640 ft |
| Capacity | 4,000 cfs |
| SOUTH FORK LONG CANYON DIVERSION PIPE AND DROP INLET |
| Diameter | 6 ft |
| Depth without 6’ x 6 ft Standpipe | 387 ft |
| Capacity | 200 cfs |
| Invert Gradient | Vertical |
| MIDDLE FORK POWERHOUSE (L.J. STEPHENSON POWERHOUSE) |
| PENSTOCK |  |
| Length | 3,653 ft or 0.7 miles |
| Diameter: Above Bifurcation | 7 ft 6 in to 9 ft O.D. |
| Diameter: Below Bifurcation | 5 ft 6 in O.D. |
| POWERPLANT |  |
| Number of Units | 2 |
| Generator Installed Capacity (Total) | 122.4 MW |
| Type of Turbine | Impulse |
| Elevation Nozzles | 2,536 ft |
| Elevation Normal Tail Water Surface | 2,529 ft |
| Maximum Static Head | 2,096 ft |
| Minimum Static Head | 1,806 ft |
| R. P. M. | 400 |
| MIDDLE FORK INTERBAY |
| DAM |  |
| Type | Gravity |
| Material | Concrete |
| Height of Dam Crest above Streambed | 70.5 ft |
| Dam Crest Length | 233 ft |
| Elevation of Dam Crest | 2,536 ft |
| Elevation of Streambed | 2,465 ft |
| Volume | 14,360 cubic yards |
| Stream Maintenance Pipe Capacity | 23 cfs |
| MIDDLE FORK INTERBAY (continued) |
| DAM (continued) |  |
| Low level Outlet Capacity at water surface 2530.0 (full reservoir) | 890 cfs |
| Roadway Width, curb to curb | 14 ft |
| Elevation of Roadway | 2,538 ft |
| SPILLWAY |  |
| Type | Gated Ogee Crest |
| Capacity (Water Surface 2534) | 36,506 cfs |
| Width of Spillway | 80 ft Gated, 60 ft Uncontrolled |
| Number of Gates | 4 |
| Type of Gates | Radial |
| Size of Gates | 20 ft x 20 ft |
| Elevation of Top of Gates | 2,530 ft |
| Elevation of Sill of Gates | 2,510 ft |
| IMPOUNDMENT |  |
| Maximum Operating Water Surface | 2,529 ft |
| Minimum Operating Water Surface | 2,502 ft |
| Normal Operating Water Surface | 2,527 ft |
| Gross Storage | 175 ac-ft |
| Dead Storage (as constructed), at Tunnel Intake lip | 2 ac-ft |
| Active Storage (as constructed) | 173 ac-ft |
| Area at Maximum Operating Water Surface | 7 acres |
| Area at Minimum Operating Water Surface | 3 acres |
| Depth at Minimum Operating Water Surface | 37 ft |
| MIDDLE FORK — RALSTON TUNNEL |
| Nominal Size / Shape | 13 ft 5 in / Horseshoe |
| Length |  |
| Total | 35,397 ft or 6.7 miles |
| Concrete Lined (Est.) | 8,245 ft |
| Steel Lined (Est.) | 245 ft |
| Maximum Discharge | 836 cfs |
| Invert Gradient | 0.0054 |
| RALSTON POWERHOUSE |
| PENSTOCK |  |
| Length | 1,670 ft |
| Diameter | 8 ft to 9 ft 6 in O.D. |
| POWERPLANT |  |
| Installed Capacity, Generator | 79.2 MW |
| Type of Turbine | Impulse |
| Elevation Nozzles | 1,186 ft |
| Static Head | 1,344 ft |
| Maximum flow | 924 cfs |
| R. P. M. | 240 |
| RALSTON AFTERBAY |
| DAM |  |
| Type | Gravity |
| Material | Concrete |
| Height of Dam Crest above Streambed | 89 ft |
| Dam Crest Length | 560 ft |
| Volume | 76,300 cubic yards |
| RALSTON AFTERBAY (continued) |
| DAM (continued) |  |
| Elevation of Dam Crest | 1,189 ft |
| Elevation of Streambed | 1,100 ft |
| Streamflow Maintenance Pipe Capacity | 155 cfs |
| Maximum Low Level Outlet Capacity at water surface el. 1179.0 (full reservoir) - calculated | 1,132 cfs |
| Roadway Width, Curb to Curb | 12 ft |
| Elevation of Roadway | 1,188.42 ft |
| SPILLWAY |  |
| Type | Gated Ogee Crest |
| Capacity at Water Surface 1186 | 171,200 cfs |
| Elevation of Top of Gates | 1,179 ft |
| Elevation of Sill of Gates | 1,149 ft |
| Crest Length | 232 ft |
| Number of Gates | 5 |
| Type of Gates | Radial |
| Size of Gates | 30’x40’ |
| IMPOUNDMENT |  |
| Gross Storage | 2,782 ac-ft |
| Active Storage | 1,804 ac-ft |
| RALSTON-OXBOW TUNNEL |
| Nominal Size / Shape | 13 ft 3 in / Horseshoe |
| Length: |  |
| Total | 403 ft or 0.08 miles |
| Concrete Lined | 343 ft |
| Steel Lined | 60 ft |
| Maximum Discharge | 1,088 cfs |
| Invert Gradient | 0.12035 |
| OXBOW POWERHOUSE |
| PENSTOCK |  |
| Length | 5 ft |
| Diameter | 9 ft I.D. |
| POWERPLANT |  |
| Installed Capacity, Generator | 6.1 MW |
| Type of Turbine | Francis |
| Elevation Runner | 1,098.5 ft |
| Static Head | 90 ft |
| Normal Tail Water Surface | 1,089 ft |
| Maximum flow | 1,025 cfs |
| R. P. M. | 200 |
| SUMMARY |
| Power and Energy Production |  |
| Total Installed Capacity (at 0.9 power factor) | 223.7 MW |
| Total Dependable Capacity (at 0.9 power factor) | 224 MW |
| Average Annual Energy Production (Based on 38 years of operation: 1967-2004) | 1,026,975 MWh |
| Maximum Total Static Head | 4,162 |
| Water Supply and Regulation |  |
| Total Gross Storage | 345,560 ac-ft |
| SUMMARY (continued) |
| Project Features |  |
| Earth and Rockfill Dams | 11,900,000 cubic yards |
| Concrete Dams and Diversions | 94,000 cubic yards |
| Tunnels and Penstocks | 23.2 miles |
| Project Completed – 1967 |
| Notes: ac-ft = acre-feet cfs = cubic feet per second ft = feet I.D. = inside diameter in = inch MW = megawatt MWh = megawatt hours O.D. = outside diameter |

# Footnotes

As constructed tunnel capacity is approximately 800 cfs, maximum discharge is limited to 400 cfs in French Meadows Powerhouse.