| Table SD B-9. Minimum Pool and Minimum Instream Flow Requirements. |
| --- |
| Facility | License Requirement |
| Minimum Pool Requirements |  |
| French Meadows Reservoir | Forecast / Folsom Reservoir 1 > 2,000,000 ac-ft 1,200,000 – 2,000,000 ac-ft < 1,200,000 ac-ft The spillway gates (tainter gates) must remain open from Nov. 15 to April 1 of each year. | Minimum Pool (ac-ft) June-Sept Oct-May 60,000 50,000 60,000 25,000 28,000 8,700 |
| Hell Hole Reservoir | Forecast / Folsom Reservoir 1 > 2,000,000 ac-ft 1,200,000 – 2,000,000 ac-ft < 1,200,000 ac-ft | Minimum Pool (ac-ft) June-Sept Oct-May 70,000 50,000 70,000 25,000 26,000 5,500 |
| Duncan Creek Diversion Pool | Maintain water surface elevation at 5,259 feet elevation. |
| Minimum Stream Maintenance Flow |  |
| Duncan Creek Diversion Dam | Forecast / Folsom Reservoir1 > 1,000,000 ac-ft < 1,000,000 ac-ft | Release (cfs) lesser of 8 or natural flow lesser of 4 or natural flow |
| French Meadows Dam | Beginning of operations to March 17,1981: |  |
|  | Forecast / Folsom Reservoir1 | Release (cfs) |
|  | > 1,000,000 ac-ft | 8 at all times |
|  | Except that total releases shall not exceed 5,800 ac-ft |
|  | < 1,000,000 ac-ft | 4 at all times |
|  | Except that total releases shall not exceed 2,900 ac-ft |
|  | March 18, 1981, and thereafter – no limitation of total release. |
| Hell Hole Dam | Beginning of operations to March 17, 1981: |
|  | Forecast / Folsom Reservoir1 > 1,000,000 ac-ft | Release (cfs) 20 June 1 – July 25 15 July 26 – Aug 5 10 Aug 6 – Oct 31 14 Nov 1 – Jan 31 20 Feb 1 – May 31 |
|  | Except that total releases shall not exceed 11,000 ac-ft. |
|  | < 1,000,000 ac-ft | 8 June 1 – Dec 1 6 Jan 1 – March 25 8 March 26 – May 31 |
|  | Except that total releases shall not exceed 5,500 ac-ft. |
|  | March 18, 1981, and thereafter: |  |
|  | Forecast / Folsom Reservoir1 > 1,000,000 ac-ft | Release (cfs) 20 May 15 – Dec 14 10 Dec 15 – May 14 |
|  |  | No limitation of total release. |
|  | < 1,000,000 ac-ft | 10 June 1 – Oct 14 6 Oct 15 – May 31 |
|  |  | No limitation of total release. |

| Table SD B-9. Minimum Pool and Minimum Instream Flow Requirements (continued). |
| --- |
| Facility | License Requirement |
| Minimum Stream Maintenance Flow (continued) |  |
| South Fork Long Canyon Diversion Dam | Forecast / Folsom Reservoir1 > 1,000,000 ac-ft < 1,000,000 ac-ft | Release (cfs) lesser of 5 or natural flow lesser of 2.5 or natural flow |
| North Fork Long Canyon Diversion Dam | Releases to maintain streamflow of 2 cfs or the natural flow, whichever is less, shall be made at all times. |
| Middle Fork Interbay | Forecast / Folsom Reservoir > 1,000,000 ac-ft < 1,000,000 ac-ft | Release (cfs) lesser of 23 or natural flow lesser of 12 or natural flow |
| Oxbow Powerhouse | Releases at Oxbow Powerhouse shall be 75 cfs at all times as measured downstream of the confluence with the North Fork of the Middle Fork. Such releases shall not cause vertical fluctuations (measured in representative section) greater than 3 feet per hour. |
| 1Forecast / Folsom Reservoir = CDWR current year forecast of unimpeded run-off of the American River to Folsom Reservoir. |