# Potential Resource Issue:

Maintenance of Project roads and trails.

# Project Nexus:

Project has the responsibility to maintain Project roads and trails.

# Potential License Condition:

- Transportation System Management Plan

# Study Objectives:

- Identify and describe Project roads and trails including condition and maintenance.

- Identify and describe non-Project roads and trails used by PCWA.

- Identify the locations along Project roads and non-project general access roads that may limit access to Project facilities from natural events.

  - Characterize vehicle use of non-Project general access roads.

  - Identify new roads or trails necessary to construct or access potential Project betterments.

  - Identify if access or the level or timing of use on Project roads and non-Project general access roads will change as a result of planned changes in future operations or maintenance activities, or during construction of potential Project betterments.

# Extent of Study Area:

The study area includes Project roads and trails and non-Project general access roads.  Project roads are identified in the Existing Project Description, Table 5-1.  Non-Project general access roads include National Forest System roads or public roads that are used by the public and by PCWA to access Project facilities or developed Project recreation facilities which are identified in the Existing Project Description, Table 5-1 and Table 5-2.

# Study Approach:

Project Roads and Trails

- Identify all Project roads and trails used by Placer County Water Agency (PCWA) to access Project facilities, including developed Project recreation facilities. A preliminary list and map of Project roads and trails is provided in the Placer County Water Agency Middle Fork American River Hydroelectric Project (FERC NO. 2079) Draft Project Description (PCWA 2006).

- Identify Project roads and trails used by the public to access dispersed concentrated use areas (see REC1 – Recreation Use and Facilities Assessment Technical Study Plan (TSP), Table REC1-1).

- Conduct a road assessment to characterize the current condition of Project roads and trails.  The road assessment survey instrument will be developed in consultation with the USDA-FS and may consist of the following:

  - Surface treatment (e.g., paved, gravel, dirt);

  - General condition;

  - Drainage features, and;

  - Safety and access features (e.g., signage, gates).

- Identify current maintenance practices, schedules, and responsibilities for Project roads and trails including road and trail maintenance agreements between PCWA and the USDA-FS.

Non-Project Roads and Trails

- Identify all non-Project roads and trails used by PCWA and the public to access Project facilities, including those that cross private land.

- Describe PCWA maintenance activities associated with non-Project roads, including snow plowing.

- Identify current non-Project roads and trails maintenance agreements between PCWA and USDA-FS.

Locations that may be at Risk to Damage from Natural Events

- Identify, describe, and map the locations along Project roads and non-Project general access roads that may limit access to Project facilities from natural events (e.g., flooding, landslides, and fire).

Vehicle Use of non-Project General Access Roads

- Describe current vehicle use of non-Project general access roads using relevant information contained in existing traffic studies and vehicle count information developed as part of the recreation visitor counts being conducted as part of REC1 – Recreation Use and Facility Assessment TSP.

- Review recreation user survey data developed as part of REC2 – Recreation Opportunities TSP to identify and characterize use of non-Project roads by visitors using Project recreation facilities.

- Summarize PCWA’s current use of non-Project general access roads through discussions with PCWA operators and maintenance personnel.

New Roads or Trails Associated with Project Betterments

- Identify, describe, and develop a GIS map showing the location of any new roads or trails that would be necessary to construct or access potential Project betterments.

Potential Changes in Level or Timing of Vehicle Use

- Describe if access or the level or timing of use on Project roads and non-Project general access roads will change as a result of planned changes in future operations or maintenance activities, or during construction of potential Project betterments.

# Schedule:

| Date | Activity |
| --- | --- |
| March through June 2008 | Collect and summarize existing data |
| July and August 2008 | Conduct field surveys |
| October through December 2008 | Summarize recreation use of non-Project roads |
| January and February 2009 | Complete data analysis and prepare draft report |
| March 2009 | Distribute draft report to Land Management TWG |
| March and April 2009 | Land Management TWG 60 day review and comment period |
| May and June 2009 | Resolve comments and prepare final report |
| July 2009 | Distribute final report to Land Management TWG and Plenary |

Level of Effort and Cost:

# To be determined.

# References:

Placer County Water Agency (PCWA). 2006. Middle Fork American River Hydroelectric Project (FERC No. 2079) Draft Project Description.