APPENDIX A

Fish Population Sampling Site Description

Table of Contents

Page

Middle Fork American River Downstream of Ralston Afterbay	1

FISH MF4.8 (Peaking Reach)	1

FISH MF14.1 (Peaking Reach)	2

Middle Fork American River from Middle Fork Interbay to Ralston Afterbay	3

FISH MF26.2 (Bypass Reach)	3

Middle Fork American River Upstream of Middle Fork Interbay	4

FISH MF36.2 (Bypass Reach)	4

FISH MF44.7 (Bypass Reach)	5

FISH MF51.8 (Comparison Reach above French Meadows Reservoir)	6

Rubicon River	7

FISH R3.5 (Bypass Reach)	7

FISH R20.9 (Bypass Reach)	8

FISH R25.7 (Bypass Reach)	9

FISH R36.2 (Comparison Reach above Hell Hole Reservoir)	10

Long Canyon Creek	11

FISH LC9.0 (Bypass Reach)	11

North Fork Long Canyon Creek	12

FISH NFLC1.9 (Bypass Reach)	12

FISH NFLC3.8 (Comparison Reach above North Fork Long Canyon Diversion)	13

South Fork Long Canyon Creek	14

FISH SFLC2.3 (Bypass Reach)	14

FISH SFLC4.2 (Comparison Reach above South Fork Long Canyon Diversion)	15

Duncan Creek	16

FISH D6.3 (Bypass Reach)	16

FISH D9.0 (Comparison Reach above Duncan Diversion)	17

North Fork of the Middle Fork American River	18

FISH NFMF2.3 (Comparison Reach)	18

North Fork American River	19

FISH NF18.4 (Bypass Reach)	19

FISH NF31.3 (Comparison Reach)	20

FISH NF53.7 (Comparison Reach)	21

Representative Photos of Project - Reservoirs and Diversion Pools	22

Ralston Afterbay	22

Middle Fork Interbay	22

French Meadows Reservoir	23

Hell Hole Reservoir	23

North Fork Long Canyon Creek Diversion Pool	24

South Fork Long Canyon Creek Diversion Pool	24

Duncan Creek Diversion Pool	25

List of Tables

Table A-1.  Reach Mesohabitat Percentages.

Table A-2.  August 2007 Water Temperature Summary.

Table A-3.  Physical Habitat Characteristics of Potential Comparison Sampling Sites.

# Middle Fork American River Downstream of Ralston Afterbay

## FISH MF4.8 (Peaking Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 474.0 | 120.0 | 56880.0 | 5.0 | 16.0 | 12.2% | 13.0% |
| 2 | Pool | S | 170.0 | 79.0 | 13430.0 | 4.0 | 12.0 | 4.4% | 3.1% |
| 3 | Pool | S | 621.0 | 201.0 | 124821.0 | 4.0 | 12.0 | 16.0% | 28.5% |
| 4 | Pool | S | 439.0 | 102.0 | 44778.0 | 9.0 | 20+ | 11.3% | 10.2% |
| 5 | Pool | S | 756.0 | 132.0 | 99792.0 | 5.0 | 16.0 | 19.5% | 22.8% |
| Total |  |  | 2460.0 | -- | 339701.0 | -- | -- | 63.5% | 77.5% |
| Average |  |  | 492.0 | 126.8 | 67940.2 | 5.4 | 14.0 | -- | -- |
| 6 | Run | S | 190.0 | 80.0 | 15200.0 | 1.2 | 2.5 | 4.9% | 3.5% |
| 7 | Run | S | 456.0 | 42.0 | 19152.0 | 1.0 | 2.0 | 11.8% | 4.4% |
| 8 | Run | S | 257.0 | 129.0 | 33153.0 | 2.5 | 5.0 | 6.6% | 7.6% |
| 9 | Run | S | 514.0 | 60.0 | 30840.0 | 2.5 | 1.5 | 13.3% | 7.0% |
| Total |  |  | 1417.0 | -- | 98345.0 | -- | -- | 36.5% | 22.5% |
| Average |  |  | 354.3 | 77.8 | 24586.3 | 1.8 | 2.8 | -- | -- |
| Grand Total |  |  | 3877.0 | -- | 438046.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |

Middle Fork American River Downstream of Ralston Afterbay

## FISH MF14.1 (Peaking Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 700.0 | 115.0 | 80500.0 | 2.5 | 7.0 | 20.7% | 22.2% |
| 2 | Pool | S | 581.0 | 130.0 | 75530.0 | 3.0 | 15.0 | 17.2% | 20.8% |
| 3 | Pool | S | 573.0 | 110.0 | 63030.0 | 9.0 | 9.0 | 17.0% | 17.4% |
| 4 | Pool | S | 303.0 | 74.0 | 22422.0 | 3.0 | 6.5 | 9.0% | 6.2% |
| Total |  |  | 2157.0 | -- | 241482.0 | -- | -- | 63.9% | 66.6% |
| Average |  |  | 539.3 | 107.3 | 60370.5 | 4.4 | 9.4 | -- | -- |
| 5 | Run | S | 564.0 | 85.0 | 47940.0 | 1.5 | 3.0 | 16.7% | 13.2% |
| 6 | Run | S | 520.0 | 125.0 | 65000.0 | 1.0 | 2.0 | 15.4% | 17.9% |
| Total |  |  | 1084.0 | -- | 112940.0 | -- | -- | 32.1% | 31.1% |
| Average |  |  | 542.0 | 105.0 | 56470.0 | 1.3 | 2.5 | -- | -- |
| 7 | LGR | S | 133.0 | 63.0 | 8379.0 | 0.8 | 1.3 | 3.9% | 2.3% |
| Total |  |  | 133.0 | -- | 8379.0 | -- | -- | 3.9% | 2.3% |
| Grand Total |  |  | 3374.0 | -- | 362801.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| LGR |

# Middle Fork American River from Middle Fork Interbay to Ralston Afterbay

## FISH MF26.2 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 232.0 | 51.0 | 11832.0 | 2.8 | 5.5 | 23.9% | 26.2% |
| 2 | Pool | S | 125.0 | 54.0 | 6750.0 | 4.5 | 7.5 | 12.9% | 14.9% |
| 3 | Pool | S | 172.0 | 45.0 | 7740.0 | 3.0 | 12.0 | 17.7% | 17.1% |
| 4 | Pool | S | 140.0 | 45.0 | 6300.0 | 2.6 | 5.0 | 14.4% | 13.9% |
| Total |  |  | 669.0 | -- | 32622.0 | -- | -- | 68.9% | 72.1% |
| Average |  |  | 167.3 | 48.8 | 8155.5 | 3.2 | 7.5 | -- | -- |
| 5 | Run | E | 57.0 | 43.0 | 2451.0 | 1.2 | 2.6 | 5.9% | 5.4% |
| 6 | Run | E | 96.0 | 35.0 | 3360.0 | 1.6 | 2.6 | 9.9% | 7.4% |
| Total |  |  | 153.0 | -- | 5811.0 | -- | -- | 15.8% | 12.8% |
| Average |  |  | 76.5 | 39.0 | 2905.5 | 1.4 | 2.6 | -- | -- |
| 7 | HGR | E | 99.0 | 45.0 | 4455.0 | 1.0 | 1.8 | 10.2% | 9.8% |
| Total |  |  | 99.0 | -- | 4455.0 | -- | -- | 10.2% | 9.8% |
| 8 | LGR | E | 50.0 | 47.0 | 2350.0 | 0.8 | 1.7 | 5.1% | 5.2% |
| Total |  |  | 50.0 | -- | 2350.0 | -- | -- | 5.1% | 5.2% |
| Grand Total |  |  | 971.0 | -- | 45238.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling; E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

# Middle Fork American River Upstream of Middle Fork Interbay

## FISH MF36.2 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 87.0 | 40.0 | 3480.0 | 2.0 | 3.5 | 16.3% | 20.2% |
| 2 | Pool | S | 80.0 | 30.0 | 2400.0 | 3.5 | 6.0 | 15.0% | 14.0% |
| 3 | Pool | S | 163.0 | 34.0 | 5542.0 | 1.7 | 4.5 | 30.5% | 32.2% |
| Total |  |  | 330.0 | -- | 11422.0 | -- | -- | 61.8% | 66.4% |
| Average |  |  | 110.0 | 34.7 | 3807.3 | 2.4 | 4.7 | -- | -- |
| 4 | Run | E | 40.0 | 30.0 | 1200.0 | 2.1 | 2.8 | 7.5% | 7.0% |
| 5 | Run | E | 60.0 | 26.0 | 1560.0 | 1.4 | 4.1 | 11.2% | 9.1% |
| Total |  |  | 100.0 | -- | 2760.0 | -- | -- | 18.7% | 16.0% |
| Average |  |  | 50.0 | 28.0 | 1380.0 | 1.8 | 3.5 | -- | -- |
| 6 | HGR | E | 104.0 | 29.0 | 3016.0 | 1.4 | 2.1 | 19.5% | 17.5% |
| Total |  |  | 104.0 | -- | 3016.0 | -- | -- | 19.5% | 17.5% |
| Grand Total |  |  | 534.0 | -- | 17198.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling; E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR |

Middle Fork American River Upstream of Middle Fork Interbay

## FISH MF44.7 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 141.0 | 39.0 | 5499.0 | 3.0 | 4.6 | 19.9% | 21.1% |
| 2 | Pool | S | 132.0 | 45.0 | 5940.0 | 2.6 | 4.2 | 18.6% | 22.8% |
| 3 | Pool | S | 215.0 | 35.0 | 7525.0 | 2.3 | 3.8 | 30.3% | 28.9% |
| Total |  |  | 488.0 | -- | 18964.0 | -- | -- | 68.7% | 72.8% |
| Average |  |  | 162.7 | 39.7 | 6321.3 | 2.6 | 4.2 | -- | -- |
| 4 | Run | E | 92.0 | 31.0 | 2852.0 | 1.6 | 3.5 | 13.0% | 10.9% |
| Total |  |  | 92.0 | -- | 2852.0 | -- | -- | 13.0% | 10.9% |
| 5 | HGR | E | 80.0 | 36.0 | 2880.0 | 1.2 | 3.6 | 11.3% | 11.1% |
| 6 | HGR | E | 50.0 | 27.0 | 1350.0 | 1.8 | 3.0 | 7.0% | 5.2% |
| Total |  |  | 130.0 | -- | 4230.0 | -- | -- | 18.3% | 16.2% |
| Average |  |  | 65.0 | 31.5 | 2115.0 | 1.5 | 3.3 | -- | -- |
| Grand Total |  |  | 710.0 | -- | 26046.0 | -- | -- | 100.0% | 100.0% |

1 LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling; E = Electrofishing

Photos of Representative Habitat Units:

| POOL | Run |
| --- | --- |
| HGR |

Middle Fork American River Upstream of Middle Fork Interbay

## FISH MF51.8 (Comparison Reach above French Meadows Reservoir)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 158.0 | 44.0 | 6952.0 | 1.3 | 2.5 | 23.9% | 24.4% |
| 2 | Pool | E | 120.0 | 39.0 | 4680.0 | 1.5 | 3.1 | 18.2% | 16.4% |
| 3 | Pool | E | 75.0 | 36.0 | 2700.0 | 1.4 | 2.5 | 11.4% | 9.5% |
| Total |  |  | 353.0 | -- | 14332.0 | -- | -- | 53.5% | 50.2% |
| Average |  |  | 117.7 | 39.7 | 4777.3 | 1.4 | 2.7 | -- | -- |
| 4 | Run | E | 105.0 | 42.0 | 4410.0 | 0.7 | 1.5 | 15.9% | 15.4% |
| 5 | Run | E | 82.0 | 42.0 | 3444.0 | 0.4 | 1.4 | 12.4% | 12.1% |
| Total |  |  | 187.0 | -- | 7854.0 | -- | -- | 28.3% | 27.5% |
| Average |  |  | 93.5 | 42.0 | 3927.0 | 0.6 | 1.5 | -- | -- |
| 6 | LGR | E | 120.0 | 53.0 | 6360.0 | 0.4 | 1.4 | 18.2% | 22.3% |
| Total |  |  | 213.5 | -- | 10287.0 | -- | -- | 32.3% | 36.0% |
| Grand Total |  |  | 660.0 | -- | 28546.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| LGR |

# Rubicon River

## FISH R3.5 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 150.0 | 55.0 | 8250.0 | * | * | 10.5% | 9.5% |
| 2 | Pool | S | 423.0 | 65.0 | 27495.0 | 2.5 | 12.0 | 29.6% | 31.7% |
| 3 | Pool | S | 105.0 | 48.0 | 5040.0 | 2.0 | 4.5 | 7.4% | 5.8% |
| 4 | Pool | S | 365.0 | 55.0 | 20075.0 | 4.5 | 14.0 | 25.6% | 23.2% |
| Total |  |  | 1043.0 | -- | 60860.0 | -- | -- | 73.1% | 70.2% |
| Average |  |  | 260.8 | 55.8 | 15215.0 | 3.0 | 10.2 | -- | -- |
| 5 | Run | S | 132.0 | 75.0 | 9900.0 | * | * | 9.3% | 11.4% |
| 6 | Run | E | 96.0 | 63.0 | 6048.0 | 1.5 | 3.2 | 6.7% | 7.0% |
| Total |  |  | 228.0 | -- | 15948.0 | -- | -- | 16.0% | 18.4% |
| Average |  |  | 114.0 | 69.0 | 7974.0 | 1.5 | 3.2 | -- | -- |
| 7 | HGR | E | 81.0 | 63.0 | 5103.0 | 1.4 | 3.1 | 5.7% | 5.9% |
| Total |  |  | 81.0 | -- | 5103.0 | -- | -- | 5.7% | 5.9% |
| 8 | LGR | E | 75.0 | 63.0 | 4725.0 | 1.0 | 2.2 | 5.3% | 5.5% |
| Total |  |  | 75.0 | -- | 4725.0 | -- | -- | 5.3% | 5.5% |
| Grand Total |  |  | 1427.0 | -- | 86636.0 | -- | -- | 100% | 100% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling; E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

Rubicon River

## FISH R20.9 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 315.0 | 70.0 | 22050.0 | * | 18.0 | 25.7% | 30.0% |
| 2 | Pool | S | 45.0 | 90.0 | 4050.0 | * | 5.0 | 3.7% | 5.5% |
| 3 | Pool | S | 300.0 | 60.0 | 18000.0 | 2.5 | 5.0 | 24.5% | 24.5% |
| 4 | Pool | S | 195.0 | 66.0 | 12870.0 | 6.0 | 12.0 | 15.9% | 17.5% |
| Total |  |  | 855.0 | -- | 56970.0 | -- | -- | 69.9% | 77.5% |
| Average |  |  | 213.8 | 71.5 | 14242.5 | 4.3 | 10.0 | -- | -- |
| 5 | Run | E | 93.0 | 36.0 | 3348.0 | 1.6 | 3.7 | 7.6% | 4.6% |
| 6 | Run | S | 165.0 | 55.0 | 9075.0 | * | 3.0 | 13.5% | 12.3% |
| Total |  |  | 258.0 | -- | 12423.0 | -- | -- | 21.1% | 16.9% |
| Average |  |  | 129.0 | 45.5 | 6211.5 | 1.6 | 3.4 | -- | -- |
| 7 | HGR | E | 111.0 | 37.0 | 4107.0 | 1.7 | 4.0 | 9.1% | 5.6% |
| Total |  |  | 111.0 | -- | 4107.0 | -- | -- | 9.1% | 5.6% |
| Grand Total |  |  | 1224.0 | -- | 73500.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling; E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR |

Rubicon River

## FISH R25.7 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 60.0 | 237.0 | 14220.0 | 2.0 | 8.0 | 14.5% | 41.3% |
| 2 | Pool | S | 33.0 | 216.0 | 7128.0 | 2.0 | 5.5 | 8.0% | 20.7% |
| 3 | Pool | S | 52.0 | 54.0 | 2808.0 | 3.5 | 6.0 | 12.6% | 8.2% |
| Total |  |  | 145.0 | -- | 24156.0 | -- | -- | 35.1% | 70.2% |
| Average |  |  | 48.3 | 169.0 | 8052.0 | 2.5 | 6.5 | -- | -- |
| 4 | Run | E | 75.0 | 29.0 | 2175.0 | 1.8 | 3.1 | 18.2% | 6.3% |
| 5 | Run | E | 69.0 | 45.0 | 3105.0 | 1.3 | 2.4 | 16.7% | 9.0% |
| Total |  |  | 144.0 | -- | 5280.0 | -- | -- | 34.9% | 15.4% |
| Average |  |  | 72.0 | 37.0 | 2640.0 | 1.6 | 2.8 | -- | -- |
| 6 | HGR | E | 62.0 | 39.0 | 2418.0 | 1.0 | 2.1 | 15.0% | 7.0% |
| Total |  |  | 62.0 | -- | 2418.0 | -- | -- | 15.0% | 7.0% |
| 7 | LGR | E | 62.0 | 41.0 | 2542.0 | 0.8 | 2.5 | 15.0% | 7.4% |
| Total |  |  | 62.0 | -- | 2542.0 | -- | -- | 15.0% | 7.4% |
| Grand Total |  |  | 413.0 | -- | 34396.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling; E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

Rubicon River

## FISH R36.2 (Comparison Reach above Hell Hole Reservoir)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 132.0 | 25.0 | 3300.0 | 2.3 | 4.6 | 19.2% | 17.2% |
| 2 | Pool | E | 130.0 | 13.0 | 1690.0 | * | * | 18.9% | 8.8% |
| 3 | Pool | E | 240.0 | 45.0 | 10800.0 | 1.8 | 3.3 | 34.9% | 56.4% |
| Total |  |  | 502.0 | -- | 15790.0 | -- | -- | 73.0% | 82.5% |
| Average |  |  | 167.3 | 27.7 | 5263.3 | 2.1 | 4.0 | -- | -- |
| 4 | Run | E | 72.0 | 7.0 | 504.0 | 0.3 | 0.6 | 10.5% | 2.6% |
| 5 | Run | E | 50.0 | 11.0 | 550.0 | 0.5 | 1.0 | 7.3% | 2.9% |
| Total |  |  | 122.0 | -- | 1054.0 | -- | -- | 17.7% | 5.5% |
| Average |  |  | 61.0 | 9.0 | 527.0 | 0.4 | 0.8 | -- | -- |
| 6 | HGR | E | 64.0 | 36.0 | 2304.0 | 0.5 | 1.3 | 9.3% | 12.0% |
| Total |  |  | 64.0 | -- | 2304.0 | -- | -- | 9.3% | 12.0% |
| Grand Total |  |  | 688.0 | -- | 19148.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | POOL |
| --- | --- |
| RUN | HGR |

# Long Canyon Creek

## FISH LC9.0 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 87.0 | 12.0 | 1044.0 | 2.5 | 5.5 | 16.0% | 11.8% |
| 2 | Pool | E | 72.0 | 16.0 | 1152.0 | 1.9 | 4.2 | 13.3% | 13.1% |
| 3 | Pool | E | 150.0 | 18.0 | 2700.0 | 0.6 | 1.8 | 27.6% | 30.6% |
| Total |  |  | 309.0 | -- | 4896.0 | -- | -- | 56.9% | 55.5% |
| Average |  |  | 103.0 | 15.3 | 1632.0 | 1.7 | 3.8 | -- | -- |
| 4 | Run | E | 63.0 | 15.0 | 945.0 | 0.8 | 1.8 | 11.6% | 10.7% |
| Total |  |  | 63.0 | -- | 945.0 | -- | -- | 11.6% | 10.7% |
| 5 | HGR | E | 67.0 | 15.0 | 1005.0 | 0.5 | 0.9 | 12.3% | 11.4% |
| Total |  |  | 67.0 | -- | 1005.0 | -- | -- | 12.3% | 11.4% |
| 6 | LGR | E | 104.0 | 19.0 | 1976.0 | 0.6 | 1.6 | 19.2% | 22.4% |
| Total |  |  | 104.0 | -- | 1976.0 | -- | -- | 19.2% | 22.4% |
| Grand Total |  |  | 543.0 | -- | 8822.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

# North Fork Long Canyon Creek

## FISH NFLC1.9 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 48.0 | 17.0 | 816.0 | 1.5 | 2.8 | 12.0% | 15.5% |
| 2 | Pool | E | 45.0 | 11.0 | 495.0 | 0.6 | 1.1 | 11.3% | 9.4% |
| 3 | Pool | E | 54.0 | 13.0 | 702.0 | 0.9 | 1.6 | 13.5% | 13.3% |
| Total |  |  | 147.0 | -- | 2013.0 | -- | -- | 36.8% | 38.3% |
| Average |  |  | 49.0 | 13.7 | 671.0 | 1.0 | 1.8 | -- | -- |
| 4 | Run | E | 78.0 | 14.0 | 1092.0 | 0.4 | 1.0 | 19.5% | 20.8% |
| Total |  |  | 78.0 | -- | 1092.0 | -- | -- | 19.5% | 20.8% |
| 5 | HGR | E | 78.0 | 12.0 | 936.0 | 0.3 | 1.0 | 19.5% | 17.8% |
| Total |  |  | 78.0 | -- | 936.0 | -- | -- | 19.5% | 17.8% |
| 6 | LGR | E | 36.0 | 13.0 | 468.0 | 0.3 | 0.6 | 9.0% | 8.9% |
| 7 | LGR | E | 60.0 | 12.5 | 750.0 | 0.4 | 0.6 | 15.0% | 14.3% |
| Total |  |  | 96.0 | -- | 1218.0 | -- | -- | 24.1% | 23.2% |
| Average |  |  | 48.0 | 12.8 | 609.0 | 0.4 | 0.6 | -- | -- |
| Grand Total |  |  | 399.0 | -- | 5259.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

North Fork Long Canyon Creek

## FISH NFLC3.8 (Comparison Reach above North Fork Long Canyon Diversion)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 85.0 | 12.0 | 1020.0 | 1.0 | 2.4 | 19.7% | 20.3% |
| 2 | Pool | E | 93.0 | 11.0 | 1023.0 | 1.6 | 0.5 | 21.6% | 20.3% |
| 3 | Pool | E | 25.0 | 16.0 | 400.0 | 0.8 | 1.7 | 5.8% | 7.9% |
| Total |  |  | 203.0 | -- | 2443.0 | -- | -- | 47.1% | 48.5% |
| Average |  |  | 67.7 | 13.0 | 814.3 | 1.1 | 1.5 | -- | -- |
| 4 | Run | E | 60.0 | 14.0 | 840.0 | 0.4 | 1.2 | 13.9% | 16.7% |
| Total |  |  | 60.0 | -- | 840.0 | -- | -- | 14% | 17% |
| 5 | HGR | E | 57.0 | 10.0 | 570.0 | 0.4 | 0.8 | 13.2% | 11.3% |
| 6 | HGR | E | 45.0 | 13.0 | 585.0 | 0.3 | 0.6 | 10.4% | 11.6% |
| Total |  |  | 102.0 | -- | 1155.0 | -- | -- | 23.7% | 23.0% |
| Average |  |  | 51.0 | 11.5 | 577.5 | 0.3 | 0.7 | -- | -- |
| 7 | LGR | E | 66.0 | 9.0 | 594.0 | 0.3 | 0.7 | 15.3% | 11.8% |
| Total |  |  | 66.0 | -- | 594.0 | -- | -- | 15.3% | 11.8% |
| Grand Total |  |  | 431.0 | -- | 5032.0 | -- | -- | 100% | 100% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

# South Fork Long Canyon Creek

## FISH SFLC2.3 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 90.0 | 15.0 | 1350.0 | 1.0 | 2.4 | 16.2% | 19.7% |
| 2 | Pool | E | 101.0 | 12.5 | 1262.5 | 1.8 | 2.5 | 18.2% | 18.5% |
| 3 | Pool | E | 96.0 | 14.0 | 1344.0 | 0.8 | 2.1 | 17.3% | 19.6% |
| Total |  |  | 287.0 | -- | 3956.5 | -- | -- | 51.7% | 57.8% |
| Average |  |  | 95.7 | 13.8 | 1318.8 | 1.2 | 2.3 | -- | -- |
| 4 | Run | E | 64.0 | 8.7 | 556.8 | 0.5 | 0.8 | 11.5% | 8.1% |
| 5 | Run | E | 52.0 | 17.5 | 910.0 | 0.4 | 0.7 | 9.4% | 13.3% |
| Total |  |  | 116.0 | -- | 1466.8 | -- | -- | 20.9% | 21.4% |
| Average |  |  | 58.0 | 13.1 | 733.4 | 0.4 | 0.8 | -- | -- |
| 6 | HGR | E | 65.0 | 10.3 | 669.5 | 0.3 | 0.9 | 11.7% | 9.8% |
| Total |  |  | 65.0 | -- | 669.5 | -- | -- | 11.7% | 9.8% |
| 7 | LGR | E | 87.0 | 8.6 | 748.2 | 0.4 | 0.7 | 15.7% | 10.9% |
| Total |  |  | 87.0 | -- | 748.2 | -- | -- | 15.7% | 10.9% |
| Grand Total |  |  | 555.0 | -- | 6841.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

South Fork Long Canyon Creek

## FISH SFLC4.2 (Comparison Reach above South Fork Long Canyon Diversion)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 112.0 | 13.0 | 1456.0 | 1.7 | 3.4 | 23.1% | 28.3% |
| 2 | Pool | E | 63.0 | 12.5 | 787.5 | 1.3 | 2.8 | 13.0% | 15.3% |
| 3 | Pool | E | 60.0 | 13.5 | 810.0 | 0.7 | 2.1 | 12.4% | 15.8% |
| Total |  |  | 235.0 | -- | 3053.5 | -- | -- | 48.5% | 59.4% |
| Average |  |  | 78.3 | 13.0 | 1017.8 | 1.2 | 2.8 | -- | -- |
| 4 | Run | E | 55.0 | 7.0 | 385.0 | 0.4 | 0.9 | 11.3% | 7.5% |
| 5 | Run | E | 47.0 | 8.5 | 399.5 | 0.5 | 1.0 | 9.7% | 7.8% |
| Total |  |  | 102.0 | -- | 784.5 | -- | -- | 21.0% | 15.3% |
| Average |  |  | 51.0 | 7.8 | 392.3 | 0.5 | 1.0 | -- | -- |
| 6 | HGR | E | 59.0 | 7.0 | 413.0 | 0.3 | 0.9 | 12.2% | 8.0% |
| Total |  |  | 59.0 | -- | 413.0 | -- | -- | 12.2% | 8.0% |
| 7 | LGR | E | 89.0 | 10.0 | 890.0 | 0.3 | 0.6 | 18.4% | 17.3% |
| Total |  |  | 89.0 | -- | 890.0 | -- | -- | 18.4% | 17.3% |
| Grand Total |  |  | 485.0 | -- | 5141.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

# Duncan Creek

## FISH D6.3 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 171.0 | 76.5 | 13081.5 | 0.8 | 2.0 | 31.6% | 63.1% |
| 2 | Pool | E | 96.0 | 25.5 | 2448.0 | 1.4 | 2.1 | 17.7% | 11.8% |
| 3 | Pool | E | 66.0 | 33.0 | 2178.0 | 1.7 | 3.0 | 12.2% | 10.5% |
| Total |  |  | 333.0 | -- | 17707.5 | -- | -- | 61.6% | 85.4% |
| Average |  |  | 111.0 | 45.0 | 5902.5 | 1.3 | 2.4 | -- | -- |
| 4 | Run | E | 69.0 | 8.0 | 552.0 | 1.0 | 2.0 | 12.8% | 2.7% |
| Total |  |  | 69.0 | 8.0 | 552.0 | 1.0 | 2.0 | 12.8% | 2.7% |
| 5 | HGR | E | 100.0 | 19.0 | 1900.0 | 0.8 | 1.2 | 18.5% | 9.2% |
| Total |  |  | 100.0 | 19.0 | 1900.0 | 0.8 | 1.2 | 18.5% | 9.2% |
| 6 | LGR | E | 39.0 | 15.0 | 585.0 | 0.5 | 1.0 | 7.2% | 2.8% |
| Total |  |  | 39.0 | 15.0 | 585.0 | 0.5 | 1.0 | 7.2% | 2.8% |
| Grand Total |  |  | 541.0 | 177.0 | 20744.5 | 6.2 | 11.3 | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

Duncan Creek

## FISH D9.0 (Comparison Reach above Duncan Diversion)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | E | 87.0 | 24.5 | 2131.5 | 0.8 | 2.3 | 19.0% | 22.0% |
| 2 | Pool | E | 109.0 | 28.0 | 3052.0 | 1.2 | 3.1 | 23.9% | 31.5% |
| 3 | Pool | E | 60.0 | 20.0 | 1200.0 | 1.5 | 3.3 | 13.1% | 12.4% |
| Total |  |  | 256.0 | -- | 6383.5 | -- | -- | 56.0% | 65.8% |
| Average |  |  | 85.3 | 24.2 | 2127.8 | 1.2 | 2.9 | -- | -- |
| 4 | Run | E | 60.0 | 15.0 | 900.0 | 0.8 | 1.4 | 13.1% | 9.3% |
| Total |  |  | 60.0 | -- | 900.0 | -- | -- | 13.1% | 9.3% |
| 5 | HGR | E | 90.0 | 11.0 | 990.0 | 0.7 | 1.5 | 19.7% | 10.2% |
| Total |  |  | 90.0 | -- | 990.0 | -- | -- | 19.7% | 10.2% |
| 6 | LGR | E | 51.0 | 28.0 | 1428.0 | 0.4 | 0.9 | 11.2% | 14.7% |
| Total |  |  | 51.0 | -- | 1428.0 | -- | -- | 11.2% | 14.7% |
| Grand Total |  |  | 457.0 | -- | 9701.5 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR | LGR |

# North Fork of the Middle Fork American River

## FISH NFMF2.3 (Comparison Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 145.0 | 33.0 | 4785.0 | * | 8.0 | 17.7% | 14.1% |
| 2 | Pool | S | 153.0 | 46.0 | 7038.0 | * | 8.5 | 18.7% | 20.7% |
| 3 | Pool | S | 162.0 | 37.0 | 5994.0 | * | 8.5 | 19.8% | 17.6% |
| 4 | Pool | S | 75.0 | 45.0 | 3375.0 | * | 3.5 | 9.2% | 9.9% |
| Total |  |  | 535.0 | -- | 21192.0 | -- | -- | 65.4% | 62.4% |
| Average |  |  | 133.8 | 40.3 | 5298.0 | -- | 7.1 | -- | -- |
| 5 | Run | E | 48.0 | 48.0 | 2304.0 | 1.4 | 3.0 | 5.9% | 6.8% |
| 6 | Run | E | 75.0 | 50.0 | 3750.0 | 1.1 | 2.6 | 9.2% | 11.0% |
| Total |  |  | 123.0 | -- | 6054.0 | -- | -- | 15.0% | 17.8% |
| Average |  |  | 61.5 | 49.0 | 3027.0 | 1.3 | 2.8 | -- | -- |
| 7 | HGR | E | 160.0 | 42.0 | 6720.0 | 0.6 | 4.2 | 19.6% | 19.8% |
| Total |  |  | 160.0 |  | 6720.0 |  |  | 19.6% | 19.8% |
| Grand Total |  |  | 818.0 | -- | 33966.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling; E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR |

# North Fork American River

## FISH NF18.4 (Bypass Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 480.0 | 12.0 | 5760.0 | 3.5 | 6.0 | 10.9% | 1.2% |
| 2 | Pool | S | 585.0 | 270.0 | 157950.0 | 7.0 | 14.0 | 13.3% | 32.9% |
| 3 | Pool | S | 309.0 | 75.0 | 23175.0 | 4.0 | 7.0 | 7.0% | 4.8% |
| 4 | Pool | S | 345.0 | 96.0 | 33120.0 | 2.8 | 4.5 | 7.9% | 6.9% |
| 5 | Pool | S | 750.0 | 50.0 | 37500.0 | 5.5 | 18.0 | 17.1% | 7.8% |
| Total |  |  | 2469.0 | -- | 257505.0 | -- | -- | 56.2% | 53.6% |
| Average |  |  | 493.8 | 100.6 | 51501.0 | 4.6 | 9.9 | -- | -- |
| 6 | Run | S | 504.0 | 186.0 | 93744.0 | 2.5 | 8.0 | 11.5% | 19.5% |
| 7 | Run | S | 216.0 | 55.0 | 11880.0 | 1.8 | 3.6 | 4.9% | 2.5% |
| 8 | Run | S | 1205.0 | 97.0 | 116885.0 | 1.2 | 3.1 | 27.4% | 24.4% |
| Total |  |  | 1925.0 | -- | 222509.0 | -- | -- | 43.8% | 46.4% |
| Average |  |  | 641.7 | 112.7 | 74169.7 | 1.8 | 4.9 | -- |  |
| Grand Total |  |  | 4394.0 | -- | 480014.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |

North Fork American River

## FISH NF31.3 (Comparison Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 630.0 | 90.0 | 56700.0 | 2.0 | 5.0 | 19.7% | 19.2% |
| 2 | Pool | S | 537.0 | 111.0 | 59607.0 | 2.0 | 6.5 | 16.8% | 20.1% |
| 3 | Pool | S | 1032.0 | 108.0 | 111456.0 | 4.0 | 11.0 | 32.3% | 37.7% |
| Total |  |  | 2199.0 | -- | 227763.0 | -- | -- | 68.8% | 77.0% |
| Average |  |  | 733.0 | 103.0 | 75921.0 | 2.7 | 7.5 | -- | -- |
| 4 | Run | S | 117.0 | 36.0 | 4212.0 | 1.0 | 2.0 | 3.7% | 1.4% |
| 5 | Run | S | 237.0 | 102.0 | 24174.0 | 1.0 | 2.0 | 7.4% | 8.2% |
| 6 | Run | S | 195.0 | 66.0 | 12870.0 | 0.6 | 1.2 | 6.1% | 4.4% |
| 7 | Run | S | 447.0 | 60.0 | 26820.0 | 0.6 | 2.1 | 14.0% | 9.1% |
| Total |  |  | 996.0 | -- | 68076.0 | -- | -- | 31.2% | 23.0% |
| Average |  |  | 249.0 | 66.0 | 17019.0 | 0.8 | 1.8 | -- | -- |
| Grand Total |  |  | 3195.0 | -- | 295839.0 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |

North Fork American River

## FISH NF53.7 (Comparison Reach)

Sampled Mesohabitat Units

| Unit Number | Unit Type1 | Sampling Method2 | Length (ft) | Width (ft) | Unit Area (ft2) | Mean Depth (ft) | Max Depth (ft) | % of Total Survey Length | % of Total Survey Area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Pool | S | 573.0 | 93.0 | 53289.0 | 6.0 | 16.0 | 31.4% | 44.4% |
| 2 | Pool | S | 405.0 | 72.0 | 29160.0 | 5.5 | 14.0 | 22.2% | 24.3% |
| 3 | Pool | S | 85.5 | 18.0 | 1539.0 | 2.0 | 4.0 | 4.7% | 1.3% |
| 4 | Pool | S | 429.0 | 61.5 | 26383.5 | 6.0 | 16.0 | 23.5% | 22.0% |
| Total |  |  | 1492.5 | -- | 110371.5 | -- | -- | 81.9% | 91.9% |
| Average |  |  | 373.1 | 61.1 | 27592.9 | -- | 12.5 | -- | -- |
| 5 | Run | E | 189.0 | 39.0 | 7371.0 | 1.2 | 2.0 | 10.4% | 6.1% |
| 6 | Run | S | 93.0 | 17.0 | 1581.0 | 1.2 | 2.0 | 5.1% | 1.3% |
| Total |  |  | 282.0 | -- | 8952.0 | -- | -- | 15.5% | 7.5% |
| Average |  |  | 141.0 | 28.0 | 4476.0 | 1.2 | 2.0 | -- | -- |
| 7 | HGR | S | 48.0 | 15.0 | 720.0 | 1.3 | 1.7 | 2.6% | 0.6% |
| Total |  |  | 48.0 | -- | 720.0 | -- | -- | 2.6% | 0.6% |
| Grand Total |  |  | 1822.5 | -- | 120043.5 | -- | -- | 100.0% | 100.0% |

1LGR = Low Gradient Riffle; HGR = High Gradient Riffle

2S = Snorkeling; E = Electrofishing

Photos of Representative Habitat Units:

| POOL | RUN |
| --- | --- |
| HGR |

# Representative Photos of Project - Reservoirs and Diversion Pools

## Ralston Afterbay

## Middle Fork Interbay

## French Meadows Reservoir

## Hell Hole Reservoir

## North Fork Long Canyon Creek Diversion Pool

## South Fork Long Canyon Creek Diversion Pool

## Duncan Creek Diversion Pool

TABLES

Table A-1.  Reach Mesohabitat Percentages.

| Study River and Site ID | Rosgen Geomorphic Reach1 (Type, Name) | Reachwide Mesohabitat Percentages by Length | Total |
| --- | --- | --- | --- |
|  |  | Pool | Run | High Gradient Riffle | Low Gradient Riffle |  |
| Middle Fork American River Downstream of Ralston Afterbay |
| Fish MF4.8 | F, MFAR-R1 | 59.5% | 30.0% | 2.7% | 7.9% | 100.0% |
| Fish MF14.1 | F, MFAR-R3 | 55.2% | 29.2% | 4.6% | 11.0% | 100.0% |
| Middle Fork American River from Middle Fork Interbay to Ralston Afterbay |
| Fish MF26.2 | Bc/F, MFAR-R4 | 43.3% | 28.6% | 21.2% | 6.9% | 100.0% |
| Middle Fork American River Upstream of Middle Fork Interbay |
| Fish MF36.2 | Ba/Fb, MFAR-R5 | 60.3% | 16.6% | 18.0% | 5.1% | 100.0% |
| Fish MF44.7 | Ba/Fb, MFAR-R5 | 60.3% | 16.6% | 18.0% | 5.1% | 100.0% |
| Fish MF51.8 | B3 | NA2 | NA2 | NA2 | NA2 | NA2 |
| Rubicon River |
| Fish R3.5 | Bc/F, RUB-R1 | 49.0% | 27.7% | 11.6% | 11.7% | 100.0% |
| Fish R20.9 | B/Fb, RUB-R2 | 46.2% | 24.7% | 25.2% | 3.9% | 100.0% |
| Fish R25.7 | C, RUB-R3 | 43.4% | 24.9% | 13.2% | 18.5% | 100.0% |
| Fish R36.2 | B3 | NA2 | NA2 | NA2 | NA2 | NA2 |
| Long Canyon Creek |
| Fish LC9.0 | F, LONG-R2 | 43.6% | 16.2% | 13.6% | 26.7% | 100.0% |
| North Fork Long Canyon Creek |
| Fish NFLC1.9 | B, NFLONG-R1 | 43.0% | 15.1% | 24.2% | 17.7% | 100.0% |
| Fish NFLC3.8 | B2-3 | NA2 | NA2 | NA2 | NA2 | NA2 |
| South Fork Long Canyon Creek |
| Fish SFLC2.3 | B, SFLONG-R1 | 40.3% | 27.7% | 15.2% | 16.8% | 100.0% |
| Fish SFLC4.2 | B3 | NA2 | NA2 | NA2 | NA2 | NA2 |
| Duncan Creek |
| Fish D6.3 | B/F, DUN-R2 | 52.8% | 14.3% | 25.2% | 7.7% | 100.0% |
| Fish D9.0 | B1-2 | NA2 | NA2 | NA2 | NA2 | NA2 |
| North Fork of the Middle Fork American River |
| Fish NFMF2.3 | F2-3/B2-3 | NA2 | NA2 | NA2 | NA2 | NA2 |
| North Fork American River |
| Fish NF18.4 | F | NA2 | NA2 | NA2 | NA2 | NA2 |
| Fish NF31.3 | F3-4 | NA2 | NA2 | NA2 | NA2 | NA2 |
| Fish NF53.7 | unknown | NA2 | NA2 | NA2 | NA2 | NA2 |
| 1For Location of Geomorphic Reaches see Map AQ 2-1. Geomorphic reaches are identified in: Placer County Water Agency (PCWA). 2007. 2006 Physical Habitat Characterization Study Report. In PCWA’s Pre-Application Document (PAD) for the Middle Fork American River Project (FERC Project No. 2079), 2005/2006 Technical Study Plans and Reports, SD G (1 of 2). |
| 2NA = Habitat percentages are unavailable for sites outside of the Project Study area. |

Table A-2.  August 2007 Water Temperature Summary.

| Study Site | Water Temperature (oF)1 |
| --- | --- |
|  | Avg | Max | Min |
| Middle Fork American River Downstream of Ralston Afterbay |
| Fish MF4.8 | 61.8 | 67.3 | 57.7 |
| Fish MF14.1 | 57.8 | 61.1 | 54.4 |
| Middle Fork American River from Middle Fork Interbay to Ralston Afterbay |
| Fish MF26.2 | 67.5 | 72.7 | 62.4 |
| Middle Fork American River Upstream of Middle Fork Interbay |
| Fish MF36.2 | 64.9 | 70.3 | 59.8 |
| Fish MF44.7 | 56.5 | 60.5 | 51.8 |
| Fish MF51.8 | 63.3 | 73.8 | 51.9 |
| Rubicon River |
| Fish R3.5 | 71.1 | 77.2 | 66.1 |
| Fish R20.9 | 60.8 | 64.7 | 57.0 |
| Fish R25.7 | 55.7 | 60.1 | 51.3 |
| Fish R36.2 | 66.1 | 72.0 | 59.8 |
| Long Canyon Creek |
| Fish LC9.0 | 60.5 | 67.8 | 54.6 |
| North Fork Long Canyon Creek |
| Fish NFLC1.9 | 60.9 | 74.2 | 52.9 |
| Fish NFLC3.8 | 58.7 | 62.4 | 54.8 |
| South Fork Long Canyon Creek |
| Fish SFLC2.3 | 58.1 | 65.6 | 51.7 |
| Fish SFLC4.2 | 55.3 | 64.0 | 48.2 |
| Duncan Creek |
| Fish D6.3 | 66.2 | 73.2 | 62.3 |
| Fish D9.0 | 63.5 | 68.8 | 60.4 |
| North Fork of the Middle Fork American River |
| Fish NFMF2.3 | 70.0 | 76.4 | 64.4 |
| North Fork American River |
| Fish NF18.4 | 64.2 | 69.6 | 60.4 |
| Fish NF31.3 | 74.7 | 82.7 | 68.8 |
| Fish NF53.7 | --2 | -- | -- |
| 1See 2006 Water Temperature Study Report (PCWA 2007c) for details and location of temperature probes |
| 2Temperature data was not available for site Fish NF53.7 |

Table A-3.  Physical Habitat Characteristics of Potential Comparison Sampling Sites.