Figure AQ 6-2.	Summary of Parameters Measured at Each Potential Barrier during 2007
Field Visits.

| Fish Passage Parameters Measured (Abbreviations Shown on Schematics1 Below) |
| --- |
| Falls | Chutes | Cascades | Critical Riffles |
| Width of channel/water at top of crest | Width of water at crest and in chute | Also measure the following for each chute/ fall | Width of riffle |
| Water depth at crest (dWc) | Water depth at crest (dWc) | Resting pool width, length, and depth if resting pools are present. | Depth across riffle |
| Water velocity at crest (VWc) | Water velocity at crest (VWc) | Air entrainment % | Velocity across riffle |
| Angle of water at crest (± θWc) | Angle of water at crest (± θWc) | Turbulence (passable or not) |  |
| Fall height (FH) | Chute height (H) |  |  |
| Depth of plunge pool (dpp) | Depth of water in chute (dW) |  |  |
| Depth of plunging water (dp) | Velocity of water in chute (VWs) |  |  |
| Distance from crest to plunge (Xp) | Length of chute slope (LS) |  |  |
| Distance from plunge to standing wave (XSW) | Slope of chute passage area (Sp) |  |  |
|  | Depth of plunge pool (dpp) |  |  |

| Fall Measurements | Chute Measurements |
| --- | --- |

1Powers, P. D. and J. F. Orsborn.  1985.  Analysis of Barriers to Upstream Migration: An Investigation of the Physical and Biological Conditions Affecting Fish Passage Success at Culverts and Waterfalls. BPA Report No. DOE/BP-36523-1.