Table AQ 11-5.	Summary of In-Situ Stream Measurements Collected During the Spring 2007 Sampling Event

| Sample ID | Location Name | Date | Temperature (°C) | Dissolved Oxygen (mg/L) | Specific Conductance (µS/cm at 25 °C) | pH | Sample Water Depth1 (m) | Secchi Depth2 (m) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Duncan Creek |  |  |  |  |  |  |  |  |
| DC-1 RM8.5 | Duncan Creek above diversion | 5/22/2007 | 7.24 | 8.9 | 57 | 7.6 | 0 |  |
| DC-2 RM8.0 | Duncan Creek below diversion | 5/22/2007 | 7.97 | 8.8 | 57 | 7.9 | 0 |  |
| DC-3 RM0.0 | Duncan Creek above Middle Fork American River confluence | 5/17/2007 | 11.16 | 6.3 | 67 | 8.2 | 0 |  |
| Middle Fork American River |  |
| MFAR-1 RM51.5 | Middle Fork American River above French Meadows Reservoir | 5/22/2007 | 8.23 | 9.0 | 53 | 7.7 | 0 |  |
| FM-1 (S) | French Meadows Reservoir surface (lower) | 5/30/2007 | 16.32 | 7.9 | 25 | 6.9 | 0 | 6.5 |
| FM-1 | French Meadows Reservoir sub-surface (lower) | 5/30/2007 | 7.17 | 8.2 | 23 | 6.5 | 30 |  |
| FM-2 (S) | French Meadows Reservoir surface (middle) | 5/31/2007 | 16.12 | 7.7 | 25 | 6.6 | 0 | 7.5 |
| FM-2 | French Meadows Reservoir sub-surface (middle) | 5/31/2007 | 8.25 | 8.4 | 24 | 6.5 | 20 |  |
| FM-3 (S) | French Meadows Reservoir surface (upper) | 5/31/2007 | 16.45 | 7.9 | 25 | 6.6 | 0 | 7 |
| FM-3 | French Meadows Reservoir sub-surface (upper) | 5/31/2007 | 9.89 | 8.8 | 23 | 6.6 | 15 |  |
| MFAR-2 RM 46.5 | Middle Fork American River below French Meadows Dam at gaging station | 5/22/2007 | 10.60 | 9.0 | 54 | 7.4 | 0 |  |
| MFAR-3 RM39.5 | Middle Fork American River above Duncan Creek confluence | 5/17/2007 | 13.17 | 6.3 | 66 | 7.7 | 0 |  |
| Table AQ 11-8. Summary of In-Situ Stream Measurements Collected During the Spring 2007 Sampling Event (continued). |
| Sample ID | Location Name | Date | Temperature (°C) | Dissolved Oxygen (mg/L) | Specific Conductance (µS/cm at 25 °C) | pH | Sample Water Depth1 (m) | Secchi Depth2 (m) |
| MFAR-4 RM39.0 | Middle Fork American River below Duncan Creek confluence | 5/17/2007 | 12.44 | 6.2 | 67 | 7.8 | 0 |  |
| MFAR-5 RM35.5 | Middle Fork American River above Middle Fork Interbay | 5/16/2007 | 13.25 | 8.9 | 68 | 8.4 | 0 |  |
| IR-1 RM36.0 | In Middle Fork Interbay | 5/16/2007 | 13.77 | 8.8 | 66 | 7.2 | 0 |  |
| MFAR-6 RM36.5 | Middle Fork American River below Middle Fork Interbay | 5/16/2007 | 10.02 | 9.3 | 60 | 7.7 | 0 |  |
| MFAR-7 RM26.0 | Middle Fork American River above Ralston Afterbay | 5/22/2007 | 15.44 | 8.5 | 82 | 7.4 | 0 |  |
| Ralston Afterbay Downstream |  |
| RA-1(S) | Ralston Afterbay surface | 5/29/2007 | 19.15 | 10.3 | 53 | 6.6 | 0 | 7 |
| RA-1 | Ralston Afterbay sub-surface | 5/29/2007 | 12.03 | 11.4 | 36 | 6.5 | 6 |  |
| MFAR-8 RM24.5 | Middle Fork American River below dam | 5/21/2007 | 18.76 | 8.0 | 63 | 7.0 | 0 |  |
| MFAR-9 RM24.0 | Middle Fork American River below Oxbow Powerhouse tailrace | 5/21/2007 | 15.32 | 8.9 | 66 | 7.3 | 0 |  |
| MFAR-10 RM9.0 | Middle Fork American River below the Drivers Flat Road Rafting Take-Out | 5/14/2007 | 16.53 | 9.7 | 64 | 6.8 | 0 |  |
| MFAR-11 RM0.1 | Middle Fork American River above North Fork American River | 5/16/2007 | 19.73 | 8.7 | 67 | 7.3 | 0 |  |
| NFAR-1 RM20.5 | North Fork American River below Middle Fork American River | 5/16/2007 | 18.51 | 8.7 | 72 | 7.4 | 0 |  |

| Table AQ 11-8. Summary of In-Situ Stream Measurements Collected During the Spring 2007 Sampling Event (continued). |
| --- |
| Sample ID | Location Name | Date | Temperature (°C) | Dissolved Oxygen (mg/L) | Specific Conductance (µS/cm at 25 °C) | pH | Sample Water Depth1 (m) | Secchi Depth2 (m) |
| Rubicon River |  |  |  |  |  |  |  |  |
| RR-1 RM35.8 | Rubicon River above Reservoir | 5/24/2007 | 9.60 | 10.3 | 52 | 7.8 | 0 |  |
| HH-1 (S) | Hell Hole Reservoir surface (lower) | 5/30/2007 | 14.52 | 8.5 | 28 | 7.0 | 0 | 9 |
| HH-1 | Hell Hole Reservoir sub-surface (lower) | 5/30/2007 | 6.65 | 8.7 | 27 | 6.7 | 30 |  |
| HH-2 (S) | Hell Hole Reservoir surface (middle) | 5/30/2007 | 14.72 | 8.1 | 28 | 6.9 | 0 | 11 |
| HH-2 | Hell Hole Reservoir sub-surface (middle) | 5/30/2007 | 7.99 | 8.8 | 27 | 6.7 | 30 |  |
| HH-3 (S) | Hell Hole Reservoir surface (upper) | 5/30/2007 | 12.72 | 8.8 | 29 | 7.1 | 0 | 8 |
| HH-3 | Hell Hole Reservoir sub-surface (upper) | 5/30/2007 | 7.79 | 9.0 | 26 | 6.8 | 30 |  |
| RR-2 RM30.1 | Rubicon River below dam at gaging station | 5/22/2007 | 7.13 | 9.8 | 54 | 7.1 | 0 |  |
| RR-3 RM 23.0 | Rubicon River above South Fork Rubicon River confluence | 5/23/2007 | 12.19 | 8.8 | 75 | 7.4 | 0 |  |
| SFRR-1 RM0.0 | South Fork Rubicon River above Rubicon River confluence | 5/23/2007 | 11.83 | 8.8 | 51 | 7.5 | 0 |  |
| RR-4 RM22.5 | Rubicon River below South Fork Rubicon River confluence | 5/23/2007 | 12.78 | 8.9 | 69 | 7.5 | 0 |  |
| RR-5 RM3.5 | Rubicon River above Long Canyon Creek confluence | 5/21/2007 | 16.30 | 8.4 | 75 | 6.9 | 0 |  |

| Table AQ 11-8. Summary of In-Situ Stream Measurements Collected During the Spring 2007 Sampling Event (continued). |
| --- |
| Sample ID | Location Name | Date | Temperature (°C) | Dissolved Oxygen (mg/L) | Specific Conductance (µS/cm at 25 °C) | pH | Sample Water Depth1 (m) | Secchi Depth2 (m) |
| RR-6 RM3.0 | Rubicon River below Long Canyon Creek confluence | 5/21/2007 | 16.26 | 8.4 | 72 | 7.3 | 0 |  |
| RR-7 RM0.7 | Rubicon River above Ralston Afterbay | 5/21/2007 | 19.61 | 8.6 | 71 | 7.3 | 0 |  |
| Long Canyon Creek |  |
| NFLC-1 RM3.5 | North Fork Long Canyon Creek above diversion | 5/15/2007 | 12.86 | 8.8 | 55 | 7.5 | 0 |  |
| NFLC-2 RM3.0 | North Fork Long Canyon Creek below diversion | 5/15/2007 | 13.80 | 8.7 | 54 | 7.7 | 0 |  |
| NFLC-3 RM0.0 | North Fork Long Canyon Creek above Long Canyon Creek confluence | 5/15/2007 | 10.81 | 9.2 | 63 | 7.3 | 0 |  |
| SFLC-1 RM3.5 | South Fork Long Canyon Creek above diversion | 5/15/2007 | 11.31 | 8.8 | 59 | 6.5 | 0 |  |
| SFLC-2 RM3.0 | South Fork Long Canyon Creek below diversion | 5/15/2007 | 11.68 | 9.1 | 58 | 6.6 | 0 |  |
| SFLC-3 RM0.0 | South Fork Long Canyon Creek above Long Canyon Creek confluence | 5/15/2007 | 9.51 | 9.3 | 60 | 7.2 | 0 |  |
| LCC-1 RM11.2 | Long Canyon Creek below North Fork and South Fork Long Canyon creeks confluence | 5/15/2007 | 9.61 | 9.3 | 60 | 7.3 | 0 |  |
| LCC-2 RM0.0 | Long Canyon Creek above Rubicon River confluence | 5/21/2007 | 15.14 | 8.8 | 69 | 7.5 | 0 |  |

1: Water sample was collected just below the water surface unless otherwise noted.

2: Secchi depth measurements were only collected in the reservoirs.

3: Instrument malfunction, no in-situ measurements available.