Table LAND 3-7.	Summary of PCWA’s Planned Response Actions During an Emergency at French Meadows Dam, Hell Hole Dam, and Ralston Afterbay Dam.

| Actions to Stop Inflows | Actions to Maximize Releases | Actions if Dam Failure is Imminent |
| --- | --- | --- |
| French Meadows Dam |  |  |
| Stop Duncan Creek Diversion inflows by closing diversion tunnel gate, or by sliding plywood sheets over the intake trash rack. | Increase generation at French Meadows to maximum. If this is not possible, consider opening the turbine bypass valve 100% (powerhouse damage may occur). If safe to do so, open the dam outlet works 60-inch Ring-Jet low level outlet to its maximum discharge capacity. Open the dam spillway radial gates if the water level is above the spillway crest. | Stop generation at Middle Fork, Ralston, and Oxbow powerhouses. Close the Middle Fork and Ralston penstock butterfly valves. If time allows, close the turbine shutoff valves and tailrace stoplog gates. |
| Hell Hole Dam |  |  |
| Shut down French Meadows Powerhouse to stop inflow from French Meadows Reservoir. Have the Sacramento Municipal Utilities District (SMUD) increase upstream diversions from their Rubicon Reservoir and Buck Island Reservoir into Loon Lake Reservoir to minimize inflow into Hell Hole Reservoir. | Increase generation to maximum at Middle Fork Powerhouse. If safe to do so, shut down Hell Hole Powerhouse and open the dam outlet works 48-inch Howell-Bunger discharge valve to its maximum discharge capacity (powerhouse damage may occur). Note: Hell Hole Dam has an uncontrolled or ungated spillway that cannot be regulated. | Stop generation at Ralston and Oxbow powerhouses. Close the Ralston penstock butterfly valve. If time allows, close the turbine shutoff valve and tailrace stoplog gate. |

Table LAND 3-7.	Summary of PCWA’s Actions During an Emergency at French Meadows Dam, Hell Hole Dam, and Ralston Afterbay Dam (continued).

| Actions to Stop Inflows | Actions to Maximize Releases | Actions if Dam Failure is Imminent |
| --- | --- | --- |
| Ralston Afterbay Dam |  |  |
| Shut down Middle Fork and Ralston powerhouses, if operating. Close spillway gates and/or 60-inch low level outlet Ring-Jet valve at French Meadows Dam or 48-inch low level valve at Hell Hole Dam (if open). Open Duncan Creek Diversion Tunnel gate (if closed), unless natural flows in Duncan Creek are minimal (<about 10 cfs). Request that SMUD halt substantial releases, if any, into the South Fork Rubicon River from Loon Lake and/or Gerle reservoirs. | Open all five radial spill gates at Ralston Afterbay Dam. Flows must be ramped up as slowly as possible, commensurate to the risk of overall failure to the dam. Increase generation to maximum at Oxbow Powerhouse, or open the turbine bypass valve to full open position. If necessary, open the 72-inch low level outlet valve (sediment may be released). |  |