Table REC 4-13.	Distances Between Points in Peaking Reach and Associated Water Travel Times.

| Location | River Mile | Use | Distance from Oxbow PH to Location (Miles) | Elapsed Travel Time in Hours1 (Distance/ 2.5 mph) |
| --- | --- | --- | --- | --- |
| Middle Fork American River |
| Indian Bar Rafter Access | 24.35 | Put-in | 0 | 0 |
| OXB gage | 23.10 | Gage | 1.25 | .5 |
| Fords Bar (Crossing) | 14.20 | Trail crossing | 10.15 | 4.1 |
| Ruck-a-Chucky | 9.22 | Take-out/put-in/trail crossing | 15.13 | 6.1 |
| Poverty Bar (Crossing) | 6.30 | Trail crossing | 18.05 | 7.2 |
| Mammoth Bar | 2.15 | Take-out/put-in/trail crossing | 22.20 | 8.9 |
| Confluence | 0 | Take-out/put-in | 24.35 | 9.7 |
| North Fork American River |
| Confluence | 20.95 | Take-out/put-in | 24.35 | 9.7 |
| Birdsall Access (Coffer Dam Crossing) | 17.30 | Take-out/put-in/trail crossing | 28.00 | 11.2 |
| Oregon Bar | 15.65 | Take-out | 29.65 | 11.9 |

1Travel time assumes a base flow of 200 cfs and a peak flow of approximately 1,000 cfs.  Travel time   changes depending upon the base flow and the peak flow.  For example, water travel time is faster when the base flow is higher or when the peak flow is higher.