Table TERR 4-12.	Consistency of Project Communication Lines and Powerlines with Avian Power Line Interaction Committee (APLIC) Guidelines.

| Name | Start | End | Length (Approx) | Voltage | Configuration Notes | Evaluation Criteria |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | No Avian Electrocution Risk | Potential Risk for Avian Electrocution |
|  |  |  |  |  |  | Communication Lines are Insulated | Powerlines are Insulated | Communication/Powerlines are Underground | Distance Between Conductors is Less than 60” | Distance Between Energized and Grounded Equipment on Equipment Poles is Less than 60 “ | Metal Guy Wires in Close Proximity to Energized Wires |
| Ralston Area |  |  |  |  |  |  |  |  |  |  |  |
| Ralston - Oxbow Tunnel Intake to Ralston Powerhouse Communication Line | Ralston-Oxbow Tunnel Intake | Ralston Powerhouse | 1.5 mi. | 2.4 kV | Communication line only (insulated) | X |  |  |  |  |  |
| Ralston Powerhouse to Ralston Powerhouse Butterfly Valve House Communication Line/Powerline | Ralston Powerhouse | Ralston Powerhouse Butterfly Valve House | 0.22 mi. | 4.16 kV | Three-phase distribution lines on wooden poles, with crossarms. Communication line (insulated) Equipment pole with three transformers | X |  |  | X | X | X |
| Ralston Afterbay Dam Generator Building to Ralston - Oxbow Tunnel Intake Communication Line/Powerline | Ralston Afterbay Dam Generator Building | Ralston-Oxbow Tunnel Intake Gatehouse | 0.15 mi. | 2.16 kV | Three phase distribution lines on wooden poles, with crossarms. Neutral (ground) wire strung alongside phase wires Communication line (insulated) Equipment pole with three transformers | X |  |  | X | X | X |
| Oxbow Powerhouse to Ralston Afterbay Dam Generator Building Communication Line/Powerline | Oxbow Powerhouse | Ralston Afterbay Dam Generator Building | 0.17 mi. | 2.4 kV | Three-phase distribution lines on wooden poles and one steel pole. The three phases are insulated and bound together. Equipment pole with three transformers Communication line (insulated) | X | X |  |  | X | X |
| Middle Fork Interbay Area |  |  |  |  |  |  |  |  |  |  |  |
| Middle Fork Powerhouse to Middle Fork Powerhouse Butterfly Valve House Communication Line/Powerline | Middle Fork Powerhouse | Middle Fork Powerhouse Butterfly Valve House | 0.62 mi. | 2.4 kV | Three-phase distribution lines on wooden poles, with crossarms. Equipment pole with three transformers Communication line (insulated) | X |  |  | X | X |  |
| Middle Fork Powerhouse Butterfly Valve House to Radio Repeater near Hell Hole - Middle Fork Tunnel Surge Tank (underground) Communication Line/Powerline | Middle Fork Powerhouse | Radio Repeater near Hell Hole-Middle Fork Tunnel Surge Tank | 0.34 mi. | 2.4 kV | Located underground |  |  | X |  |  |  |
| Middle Fork Powerhouse to Middle Fork - Ralston Tunnel Intake and Gatehouse Communication Line/Powerline | Middle Fork Powerhouse | Middle Fork-Ralston Tunnel Intake and Gatehouse | 0.36 mi. | 2.4 kV | Three-phase distribution lines on wooden poles. The three phases are insulated and bound together. Equipment pole with three transformers Communication line (insulated) | X | X |  |  | X |  |
| Middle Fork Powerhouse to Middle Fork American River Gage above Middle Fork Powerhouse Communication Line/Powerline | Middle Fork Powerhouse | Middle Fork American River Gage above Middle Fork Powerhouse | 0.09 mi. | 102 V | Single-phase distribution lines on wooden poles Communication line (insulated) | X |  |  |  |  |  |

Table TERR 4-12.	Consistency of Project Communication Lines and Powerlines with Avian Power Line Interaction Committee (APLIC) Guidelines (continued).

| Name | Start | End | Length (Approx) | Voltage | Configuration Notes | Evaluation Criteria |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | No Avian Electrocution Risk | Potential Risk for Avian Electrocution |
|  |  |  |  |  |  | Communication Lines are Insulated | Powerlines are Insulated | Communication/Powerlines are Underground | Distance Between Conductors is Less than 60” | Distance Between Energized and Grounded Equipment on Equipment Poles is Less than 60 “ | Metal Guy Wires in Close Proximity to Energized Wires |
| French Meadows Area |  |  |  |  |  |  |  |  |  |  |  |
| French Meadows Dam Generator Building to French Meadows Dam Outlet Works Powerline | French Meadows Dam Generator Building | French Meadows Dam Outlet Work | 0.23 mi. | 208 V | Three-phase distribution lines. At least one wire is insulated and phases are bound together. |  | X |  |  |  |  |
| French Meadows Dam Generator Building to French Meadows Dam Spillway Gates Powerline | French Meadows Dam Generator Building | French Meadows Dam Spillway Gates | 69 ft. | 208 V | Three-phase distribution lines on wooden poles and one steel pole. The three phases are insulated and bound together. |  | X |  |  |  |  |
| Hell Hole Area |  |  |  |  |  |  |  |  |  |  |  |
| French Meadows Powerhouse to French Meadows Powerhouse Penstock and Butterfly Valve House Communication Line/Powerline | French Meadows Powerhouse and switchyard | Butterfly valve house at the top of French Meadows Powerhouse Penstock | 0.1 mi | 2.4 kV | Three-phase distribution lines. At least one wire is insulated and phases are bound together. Communication line (insulated) | X | X |  |  |  |  |
| French Meadows Powerhouse and Switchyard to Hell Hole-Middle Fork Tunnel Gatehouse, Dormitory Facility, Operator Cottages and Hell Hole Powerhouse Communication Line/Powerline | French Meadows Powerhouse and Switchyard | Hell Hole-Middle Fork Tunnel Gatehouse, Dormitory Facility, Operator Cottages and Hell Hole Powerhouse | 2.29 mi. | 12 kV | Most of the extent consists of three-phase distribution lines on wooden poles with crossarms. A portion of the powerline leading to the Hell Hole Powerhouse has three-phase distribution lines with conductors mounted vertically on the poles (no crossarms). There are several equipment poles and structures throughout the extent of this line, especially large structures at the Hell Hole Substation and the Hell Hole Powerhouse. Communication line (insulated) | X |  |  | X | X | X |
| Dormitory and Cottages Water Supply Tank Powerline | Water Supply Tank | Dormitory and Cottages | 0.08 mi. | 2.4 kV | Single-phase distribution lines on wooden poles |  |  |  |  |  | X |
| Hell Hole Powerhouse to Rubicon River Gage and Weir below Hell Hole Dam Communication Line/Powerline | Hell Hole Powerhouse | Rubicon River Gage and Weir below Hell Hole Dam | 0.12 mi. | 12 kV | Three-phase distribution lines on wooden poles, with small crossarms Communication line (insulated) | X |  |  | X |  | X |