Examples of Communication Line and Powerline Configurations

Examples of Equipment Poles and Structures

# Text boxes

Oxbow Powerhouse to Ralston Afterbay Dam Generator Building Communication Line/Power Line:

This photograph shows both insulated communication lines and an insulated and bundled three-phase powerline mounted on the same pole. This configuration does not represent a risk for avian electrocution.

French Meadows Powerhouse and Switchyard to Hell Hole-Middle Fork Tunnel Gatehouse, Dormitory Facility, Operator Cottages and Hell Hole Powerhouse Communication Line/Powerline:  This photograph shows a portion of the powerline leading to the Hell Hole Powerhouse with uninsulated three-phase distribution lines and conductors mounted vertically on the poles (no crossarms).  This configuration poses a potential risk for avian electrocution.

French Meadows Powerhouse and Switchyard to Hell Hole-Middle Fork Tunnel Gatehouse, Dormitory Facility, Operator Cottages and Hell Hole Powerhouse Communication Line/Powerline:  This photograph shows a portion of the powerline leading to the French Meadows Powerhouse  that has uninsulated three-phase distribution lines with conductors mounted horizontally on crossbars.  Note also the guy wires located in proximity to the phases.  This configuration poses a potential risk for avian electrocution.

Hell Hole Powerhouse to Rubicon River Gage and Weir below Hell Hole Dam Communication Line/Powerline: This photograph shows another uninsulated three-phase distribution line with conductors mounted horizontally on crossbars.  This configuration poses a potential risk for avian electrocution.  (Insulated communication lines are also mounted on the pole below the cross bars.)

French Meadows Powerhouse and Switchyard to Hell Hole-Middle Fork Tunnel Gatehouse, Dormitory Facility, Operator Cottages and Hell Hole Powerhouse Communication Line/Powerline:  This photograph shows an equipment pole with three metal transformers near the Hell Hole-Middle Fork Tunnel Gatehouse.  This equipment pole design poses a potential risk for avian electrocution.

Ralston Afterbay Dam Generator Building to Ralston - Oxbow Tunnel Intake Communication Line/Powerline:  This photograph shows an equipment pole with three metal transformers near the Hell Hole-Middle Fork Tunnel Gatehouse. This equipment pole design poses a potential risk for avian electrocution.

French Meadows Powerhouse and Switchyard to Hell Hole-Middle Fork Tunnel Gatehouse, Dormitory Facility, Operator Cottages and Hell Hole Powerhouse Communication Line/Powerline:  This photograph shows a large equipment structure at the Hell Hole Substation. This equipment pole design poses a potential risk for avian electrocution.

French Meadows Powerhouse and Switchyard to Hell Hole-Middle Fork Tunnel Gatehouse, Dormitory Facility, Operator Cottages and Hell Hole Powerhouse Communication Line/Powerline:  This photograph shows a large equipment structure at the Hell Hole Powerhouse. This equipment pole design poses a potential risk for avian electrocution.